## Slide 1: Communication Networks Introduction
1
DR.Eslami
Department of Electrical Engineering
Islamic Azad University،Science And Research Branch

## Slide 2: Introduction
2
The course introduces the underlying concepts and principles of Communication Networkss.
It presents different components of a network and how
these components fit together.
The layers of functionalities implemented in network nodes are investigated and the underlying design concepts are discussed.
The course is designed at a graduate level with practical
assignments and short projects

## Slide 3: Text References
3
Required Textbook
  Andrew Tanenbaum. Computer Networks, Sixth Edition, Prentice Hall
Additional textbooks and References
  A. Leon-Garcia & I. Widjaja, Communication Networks, McGraw Hill
  W. Stallings. Data and Computer Communications. Prentice Hall.
  J. Walrand. Communication Networks: First Course. Aksen Associates.
  D. Comer. Internetworking with TCP/IP, Volume I, Prentice Hall.
  W. Stevens. TCP/IP Illustrated: The Protocols, Vol 1. Addison-Wesley.
  D. Comer. Computer Networks and Internets. Prentice Hall.
  L. Peterson and B. Davie. Computer Networks: A Systems Approach. Morgan Kaufman.
Some of the course material are presented from other sources

## Slide 4: Course Outline
4
Introduction.
The Physical Layer.
The Data Link Layer.
The Multiple Access Sub-Layer.
The Network Layer.
The Transport Layer.
The Application Layer.

## Slide 5: Brief History of Communication Networkss
1961-1964 Idea of store and forward distributed communication in packet
networks by L. Kleinrock, D. Watts and P. Baran
  More suitable for computer communication
  More resilient to node failure
Creation of ARPANET in late 1960’s
  To build a network that withstands destruction of some of its nodes
  First Network started operation in 1969
5

## Slide 6: History of Internet
Communication Networkss
8
https://www.vox.com/a/internet-maps
ARPANET, the precursor to the modern internet, was an academic research project funded by the Advanced Research Projects Agency, a branch of the military known for funding ambitious research projects without immediate commercial or military applications

## Slide 7: 1970: ARPANET expands
By the end of 1970, ARPANET had grown to 13 nodes

## Slide 8: 1973: ARPANET goes international
In 1973, the ARPANET became international, with a satellite link connecting Norway and London to the other nodes in the United States. Hawaii also joined the network by satellite. At this point, the network had around 40 nodes.

## Slide 9: 1982: the ARPANET community grows
By 1982, the network had about 100 nodes.

## Slide 10: 1984: ARPANET becomes the internet
In 1984, ARPANET network operators decided that the network should be reorganized as a decentralized "network of networks."
Under this scheme, different networks would be controlled by different organizations, but all the
networks able to communicate using shared standards, forming a shared "internet."

## Slide 11: 1984: ARPANET becomes the internet
A set of standards known as TCP/IP was developed.
On January 1, 1983, the ARPANET switched to using TCP/IP, marking the birth of
the modern internet.

## Slide 12: NSFNET: The first internet backbone
In 1986, the US National Science foundation agency created a TCP/IP-based network called NSFNET to link supercomputing centers together and allow researchers across the country to use them.
The NSFNET became the internet's "backbone," the high-speed, long-distance network that allowed different parts of the internet to communicate.

## Slide 13: The internet becomes a global network
In 1993, the internet was still dominated by the United States, but it was becoming a truly global network. This is a map of information flow on Usenet, a bulletin board application.

## Slide 14: The privatization of the internet backbone
In 1994, the internet backbone was privatized to several competitive service providers.

## Slide 15: Internet Growth

## Slide 16: Internet Growth

## Slide 17: Global Usage of Internet

## Slide 18: Global Usage of Internet

## Slide 19: Computer Networks
Old: Single powerful computer, many local terminals for interaction
Now: Many autonomous computers interconnected to do the job

## Slide 20: Applications of Computer Networks
Access to Information
  Web Browsing
  Online navigation
Person to Person Communication
  Instant Messaging
  Social Networks
  Video Calling
Electronic Commerce
  Business to Consumer (B2C)
  Business to Business (B2B)
  Government to consumer (G2C)
Entertainment
  IPTV
Internet of Things

## Slide 21: Types of Communication Networkss
Broadband Access Networks
Mobile and Wireless Access Networks
Content Provider Networks
Transit Networks
Enterprise Networks

## Slide 22: Types of Networks
PAN (Personal Area Network)
  Network with a short range
  Example: Bluetooth connections

## Slide 23: Types of Networks
LAN (Local Area Network)
  Network usually within a building
  Restricted Size, delay
  Rate: 10Mbps to 10Gbps
  Channel allocation: Static or dynamic
  Examples: Ethernet (IEEE 802.3),

## Slide 24: Types of Networks
MAN (Metropolitan Area Network)
  A network within a city

## Slide 25: Types of Networks
WAN (Wide Area Network)
  A network with large area
  A WAN can span a country, several countries or a it can have a global
coverage
  Example:
    FLAG Network (Global)
    See: https://www.submarinecablemap.com/

## Slide 26: FLAG Europe-Asia (FEA)
WAN (Wide Area Network)
  A network with large area
  A WAN can span a country, several countries or a it can have a global
coverage
  Example:
    TIC Network (One Country)
    FLAG Network (Global)

## Slide 27: Overview of Internet Architecture

## Slide 28: Network Protocol Design Goals
Reliability
Resist bit errors
Find a path to destination
Resource Allocation
Properly share resources
Flow control
Manage the quality of service
Evolvability
Cope with growth
Security
Confidentiality
Authentication

## Slide 29: Network Operation Principles
Functionality of most networks are organized as a series of layers
Each layer is implemented by an entity
Peers: two communicating entities (within the same layer)

## Slide 30: Network Operation Principles

## Slide 31: Network Software
Protocol: An agreement on rules and procedures between two communicating parties on how the communications is to proceed.
Service: set of primitives (operations) that a layer provides to the above layer

## Slide 32: Network Software
Headers/Trailers may be needed to allow implementation of a protocols

## Slide 33: Service Categories and Reliability
Communication Networkss
33
Service Categories:
  Connection oriented
    Phone conversation
    Telnet / remote login / FTP
  Connectionless
    Postal system
    Email
Service Reliability
  Reliable: never loose data
    Acknowledgements /
retransmission
  Unreliable: data may be lost
    No acknowledgements
    Datagram service

## Slide 34: Open System Interconnect (OSI) Reference Model
34

## Slide 35: TCP/IP Reference Model
Originated from ARPANET
35

## Slide 36: TCP/IP Reference Model
Link Layer: Move packets from one node to the next.
36

## Slide 37: TCP/IP Reference Model
Internet Layer: Find the best path for packets to reach their
destination.
37

## Slide 38: TCP/IP Reference Model
38
Transport Layer: It is designed to allow peer entities on the source
and destination hosts to carry on a conversation.
Transport of data can be “Reliable” or “Un-Reliable”.

## Slide 39: TCP/IP Reference Model
39
Application Layer: E-mail, Web, Remote Connection and many other
protocols.

## Slide 40: Comparing OSI and TCP/IP
Data
Networks 43
OSI:
  Top-down design methodology
  The concepts clearly distinguishes
    Services (specification)
    Interfaces
    Protocols (implementation)
  Network layer supports both connectionless and connection-oriented communication
  Transport layer supports only connection-oriented service !!
TCP / IP
  Bottom-up approach; grew out of practice
  Not a general protocol stack
  Host-to-network layer is actually an interface description

## Slide 41: Critics on OSI model
Bad timing.
Bad technology.
  Too many layers (Competition
with 7 layer IBM SNA! stack)
  Overloaded (L2, L1) and empty (L5, L6) layers
  Too difficult to understand and implement
  Initially ignored connectionless protocols
Bad implementations.
  Early implementations were huge, unwieldy, and slow.
Bad politics
  TCP/IP as part of UNIX, widely available, useful and open
  OSI as a creature of telecom ministers/big telecom companies
41

## Slide 42: Model of Choice
We will follow a hybrid, 5-layer model in this course
Data Link Layer includes Multiple Access Control (MAC) functionalities, but noting the importance of MAC, we will devote a special section to it.
42

## Slide 43: Standardization: Who’s Who
43
Telecommunication world
  ITU: International Telecommunication Union
International standards
  ISO: Int. Organization for Standardization (1946)
  ANSI: American National Standards Institute
  IEEE: Inst. of Electrical and Electronic Engineers
Internet
  IAB: Internet Activities Board
  IETF: Internet Engineering Task Force
  IRTF: Internet Research Task Force

## Slide 44: Communication Networkss Physical Layer
DR.Eslami
Department of Electrical Engineering
Islamic Azad University،Science And Research Branch

## Slide 45: Physical Layer
Physical Layer is responsible for delivering a stream of symbols (usually a
stream of 1’s and 0’s) from a source over a channel to a destination.
Information theory shows that there are limitation for delivering information
over a channel
Maximum Data Rate of a band limited noiseless channel:
C=2W*log2(V) bits/sec
where V is number of discrete signal levels, W is channel bandwidth
For Noisy channels: C=Wlog2(1+SNR) bits/sec
Example: A channel with a bandwidth of 4kHz and SNR=30dB can carry
40kbps at most

## Slide 46: Physical Layer
Important communication Media:
  Guided Transmission Media
    Twisted Pair
    Coaxial Cable
    Power Lines
    Fiber Optics
  Wireless Transmission
    Radio/Microwave Transmission
    Millimeter Wave Transmission
    Light wave Transmission
    Satellite Communication
      Geostationary
      Medium Orbit Satellites
      Low Earth Orbit Satellites

## Slide 47: Twisted Pair
Twisted Pair cable is used in telephone networks and Communication Networkss
Attenuation depends on distance, frequency and cable type

## Slide 48: Twisted Pair
Twisted Pair is also used
for LAN cabling

## Slide 49: Twisted Pair
Twisted pair cables are standardized and used in Communication Networkss
ategory | Max. Data Rate | Bandwidth | Max. Distance | Usage
Category 1 | 1 Mbps | 0.4 MHz |  | Telephone and modem lines
Category 2 | 4 Mbps | 4 MHz |  | LocalTalk & Telephone
Category 3 | 10 Mbps | 16 MHz | 100 m | 10BaseT Ethernet
Category 4 | 16 Mbps | 20 MHz | 100 m | Token Ring
Category 5 | 100 Mbps | 100 MHz | 100 m | 100BaseT Ethernet
Category 5e | 1 Gbps | 100 MHz | 100 m | 100BaseT Ethernet, residential homes
Category 6 | 1 Gbps | 250 MHz | 100 m (10Gb at 37 m) | Gigabit Ethernet, commercial buildings
Category 6a | 10 Gbps | 500 MHz | 100 m | Gigabit Ethernet, commercial buildings
Category 7 | 10 Gbps | 600 MHz | 100 m | 10 Gbps Core Infrastructure
Category 7a | 10 Gbps | 1000 MHz | 100 m (40Gb at 50 m) | 10 Gbps Core Infrastructure
Category 8 | 25 Gbps (Cat8.1) 40 Gbps (Cat8.2) | 2000 MHz | 30 m | 25 Gbps/40 Gbps Core Infrastructure

## Slide 50: Coaxial Cable
Better shielding than twisted pair
Lower attenuation & cross talk
Can carry 1~2 Gbps in 1 km
Telco’s used it for their backbone communication. It is replaced by fiber
optics.
Cable TV companies use it for TV and data delivery services.

## Slide 51: Cable TV Networks

## Slide 52: Hybrid Fiber Coax Architecture
Combination of fibers and coaxes used to deliver the service
Lasers are intensity modulated using the analogue RF signal
Data Over Cable Service Interface Specification (DOCSIS) series of standards were developed to allow data service delivery over the TV cable network.
DOCSIS 3.0 is the latest version of the standard (2007) which also supports
QoS

## Slide 53: Power Lines
Power Lines Carrier Communication Systems are used by Electric companies for transmission of control and dispatching data over power lines.

## Slide 54: Power Lines
Power Lines can be used for broadband data communication inside
home.
HomePlug AV2 standard supports up to 1Gbps

## Slide 55: Light Refraction
From less dense to more dense medium
From more dense to less dense medium

## Slide 56: Light Reflection

## Slide 57: Optical Fiber Structure

## Slide 58: Fiber types
Multi-mode
Fiber
Single-mode
Fiber

## Slide 59: Fiber Types: Single Mode and Multi Mode

## Slide 60: Fiber Optic Connector (LC/LC)
LC Adaptor

## Slide 61: Types of fiber connectors

## Slide 62: Attenuation
Typical Attenuation for Multimode fiber:
  3 dB/km @ 850 nm
  1 dB/km @ 1300 nm
Typical Attenuation for Single mode fiber:
  0.4 dB/km @ 1310 nm
  0.25 dB/km @ 1550 nm

## Slide 63: Fiber Optic Cable: Advantages
Fiber can handle much higher data rates than copper
  C-Band: 1530-1565 nm
  Frequency Range: 191 THz to 196 THz => 5 THz of bandwidth
Fiber has low loss of signal power (attenuation), so fewer repeaters are needed for fiber optic links compared to copper based links
Fibers are difficult to tap and therefore excellent for
security

## Slide 64: Fiber Optic Advantages
Fiber is not affected by power surges, electromagnetic interference
or power failure, or corrosive chemicals in the air
  Photons of light in a fiber do not affect each other as they have no electrical charge, and they are not affected by stray photons outside the fiber
  In the case of copper, electrons move through the cable and these are
affected by each other and by electromagnetic fields outside the cable
Fibers are thin and lightweight, allowing more cables to fit into a given area
  1000 twisted pair cables 1 km long = 800kg
  2 optical fiber cables 1km long = 100kg (allows transfer of much more data)

## Slide 65: Light source
Sending device called “light
source”
Light source
  Light-emitting diode (LED)
    Cheap but unfocused
    Short distance
  Laser diode (LD)
    More expensive than LEDs
but focused
    Preserve the signal (long
distance)
    Most communication
systems use LD

## Slide 66: Light Sources
Lasers produce light in a more confined region of spectrum

## Slide 67: Light Sources
Lasers can generate pulses with shorter duration in time. Therefore, higher modulation rates can be achieved with lasers.

## Slide 68: Light Receiver
Receiving device called “photosensitive cell” (photodiode)
Photodiode converts optical signal to electrical signal

## Slide 69: Light wave transmission system - overview

## Slide 70: Wireless Communication
Main Drivers
  Communication without a physical attachment such as wires or fibers.
  Mobility of users
  Ease of deployment

## Slide 71: Electromagnetic Spectrum

## Slide 72: Wireless Communication
Radio range of frequencies (10KHz to 10MHz) usually used for broadcast
communication
  Long range, low attenuation, reflection from ionosphere
Microwave range of frequencies (10MHz to 10GHz) usually used for point to
point long distance transmission and local two-way communications
  Medium range, affected by rain and weather conditions. Subject to multipath
fading.

## Slide 73: Spectrum Allocation

## Slide 74: Spectrum Allocation

## Slide 75: Spectrum Regulations
Most radio frequency bands are regulated. Using frequency spectrum for commercial purposes is usually subject to a regulatory fee.
There are license free bands available in most countries (ISM
bands)

## Slide 76: Free Space Optical Communication
Idea: Light as the information carrier for free space communication

## Slide 77: FSO: Outdoor Applications

## Slide 78: FSO: Outdoor Applications

## Slide 79: FSO: Indoor Applications

## Slide 80: FSO: Indoor Applications
Visible Light Communication (VLC)

## Slide 81: Satellite Communication
Satellites can be used as a wireless node in the sky that can
receive, amplify, process and transmit communication signals
They are mainly used in three orbit ranges and therefore have
different rotation period around earth.

## Slide 82: Satellite Communication
Satellites generally have multiple transponders each with a given
bandwidth/capacity for data transport
They usually use “spot-beams” to focus their transmission on a given
region.
Most communication satellites are at Geostationary orbit
Satellite operational frequency ranges:

## Slide 83: Satellite Communication - VSAT
Very Small Aperture Terminals (VSAT)
  Small terminals that communicate to each other through a Geostationary satellite
and a HUB.
  VSAT can be used to provide voice and data connectivity to remote locations with
no land-based telecommunication infrastructure
  Data rate of links ranges from 4 kb/s to 100 Mb/s

## Slide 84: Satellite Communication - VSAT

## Slide 85: Medium Earth Orbit Satellites (MEO)
Rotate at 6 hours or less around earth
Global Positioning using 31 Satellites at about 20,000 km

## Slide 86: How GPS works

## Slide 87: Low Earth Orbit Satellites (LEO)
Satellites orbiting earth below 2000 km with a rotation time of 128
minutes or less
Many satellites are needed to cover the earth for providing
communication services (Mobile phone, Internet access)
Starlink, Telesat, and Oneweb/Airtel are some of the companies that
have satellite systems to provide global voice and data services.

## Slide 88: Satellite Communication
In some LEO satellite systems such as Iridium, satellites are
relaying and switching the data from source to destination
In some other satellite systems such as Globalstar, satellites relay the signal to their ground station and switching is done by a terrestrial network. The advantage is that much of the complexity is on the ground and satellites are simpler.

## Slide 89: LEO Satellites
Starlink currently has more than 3500 satellites

## Slide 90: Satellites Versus Fiber
Optical communication is the dominant technology for transmission
of voice and data.
From office LANs to intercontinental communication networks,
optical communication systems are used as a cost effective solution.
Satellite communication serves some key demands
  Networks that require rapid deployment (disaster recovery, military
applications)
  Communication in places where terrestrial networks are not well
developed (jungles, countries with many islands, oil stations in the sea)
  Broadcasting (TV, Radio)

## Slide 91: Baseband Transmission

## Slide 92: Passband Transmission

## Slide 93: Multiplexing
In telecommunications and computer networks, multiplexing (sometimes contracted to muxing) is a method by which multiple analog message signals or digital data streams are combined into one signal over a shared medium.
The aim is to share an expensive resource.
Multiplexing originated in telegraphy in the 1870s, and is now widely applied in communications..
The multiplexed signal is transmitted over a communication channel, which
may be a physical transmission medium.
The multiplexing divides the capacity of the high-level communication channel into several low-level logical channels, one for each message signal or data stream to be transferred.
A reverse process, known as demultiplexing, can extract the original channels
on the receiver side.
A device that performs the multiplexing is called a multiplexer (MUX), and a
device that performs the reverse process is called a demultiplexer (DEMUX).

## Slide 94: Frequency Division Multiplexing
Information from multiple sources can be multiplexed in frequency domain by assigning different carriers to different sources.
Usually there is a guard band between different frequency bands
Orthogonal Frequency Division Multiplexing (OFDM) allows us to use different frequency bands for transmission of data in a more efficient way
OFDM is used in wireless networks, cable networks and twisted pair networks.

## Slide 95: Wavelength Division Multiplexing
Several independent streams of data each carried in a different wavelength can be multiplexed in optical domain and transmitted over a single fiber.
This technology has drastically increased the capacity and lowered to cost of transmission networks

## Slide 96: Time Division Multiplexing
Different sources of data can be transmitted by dividing time into
different slots and using each slot for a stream of data
TDM is widely used in optical networks and wireless networks.

## Slide 97: Code Division Multiplexing
A techniques which allows for a new multiple access mechanism and is proving to be very effective for mobile communication. (Used in 2G and 3G mobile systems)
Time division: TDM
  each speaker gets its turn
Frequency division: FDM
  concurrent speakers separated far enough
Code Division Multiplexing (CDM)
  every speaker speaks a different language at the same time
Key idea:
  Each station uses the entire frequency band but uses a different code.

## Slide 98: Principles of CDMA
https://networkencyclopedia.com/code-division-multiple-access-cdma/

## Slide 99: Code Division Multiplexing
Each bit time interval is divided into m slots called chips
Each transmitter uses a unique chip sequence to send 1 and its inverse to
send 0.
  Send 1 as: 1 1 -1 -1 1 -1 1 -1
  Send 0 as: -1 -1 1 1 -1 1 -1 1
Chips are chosen to have these properties:
i1
i1
i
i i
m
m
S  S  1  s2  1
m
m
S T  1  s t  0

## Slide 100: CDMA Example

## Slide 101: CDMA Example

## Slide 102: CDMA Example
Example:

## Slide 103: Code Division Multiplexing
CDMA Spectrum

## Slide 104: Code Division Multiplexing
Practical issues:
  Keys should be known in advance
  Power Control:
    Senders should be received with same power
    Send with inverse power of received signal strength
  Synchronization: what if senders are not synchronized:
    Lock into the ‘wanted’ channel
    Other channels will be received as background noise

## Slide 105: Telephone system
Public Switched Telephone Network (PSTN)
  A complex network that spans the globe and enables voice and data
communication.

## Slide 106: Old Telephone Switches

## Slide 107: Elecrtromechanical Switching

## Slide 108: Modern Switching Center

## Slide 109: Telephone system
Telephone system organization: hierarchical network with three important
components:
  Local loops:
  Switching centers:
  Trunks: connecting switching offices using various transmission technologies

## Slide 110: Switch Hierarchy, an example

## Slide 111: Telephone Switch
SLIC
SLIC
SLIC
SLIC
SLIC
SLIC
SLIC
SLIC
SLIC
SLIC
TDM Switch
E1 Mux
Control Unit
Timing Unit

## Slide 112: Dual-Tone Multi-Frequency Signaling
DTMF is a telecommunication signaling system using the voice- frequency band over telephone lines between telephone equipment and other communications devices and switching centers.
Pressing a key sends a combination of the row and column
frequencies.
Telephone switching centers detect the received tones to extract the
pressed key.

## Slide 113: SLIC/CODEC
Important User Side Functions
  Battery supply to subscriber
line
  Overvoltage protection
  Off/On hook detection
  Ring Generation
  Tone Detection
  Tone Generation
  Hybrid
  Testing
Important Network Side
Function
  PCM Coder/Decoder
  Filtering and Amplification
  Compression/Decompression

## Slide 114: Telephone Modem
Modem: A device that receives a stream of digital bits and sends/receives it
properly from the transmission medium (such as twisted pair)
Transmission problems:
  Attenuation and Delays which are frequency dependent
  Noise (Thermal Noise, Impulse Noise, etc)
  Cross talk, caused by inductive coupling of wires
For voice band modems, data rate is limited by PSTN sampling process and
loop conditions

## Slide 115: Voice band modem standards
Important voice band modem standard:
  V.32: 9600 bps : 4 bits / baud
  V.32 bis: 14.4 kbps : 6 bits / baud
  V.34: 28.8 kbps (Using QAM Constellation)
  V.90: 56 kbps DS, 33.6 kbps US
  V.92: 56 kbps DS, 48 kbps US
Maximum modem data rate for connection over normal PSTN networks:
33.6kbps (limited by quantization noise)
Rates achieved by V.90 and V.92 standards is achieved when connecting to
ISPs with digital network connection
Compression schemes:
  MNPs : run-length encoding (runs of zero’s may be very common)
  V.42 bis : Ziv-Lempel compression

## Slide 116: Asymmetric Digital Subscriber Line (ADSL)
Objective: Offering data services without impacting the voice service on twisted pair
Central Office (CO) side:
  Use splitter to feed low pass part to the voice switch while the higher frequencies to the feed the DSLAM
Customer Premise End (CPE)
  Use splitter or in-line filters to feed the low pass part of the spectrum to the telephone and the high pass part to the CPE ADSL modem
ADSL signal power spectrum is defined carefully to reduce cross talk into other services

## Slide 117: ADSL
Uses Discrete Multi tone technique (DMT) as the modulation scheme.
Idea: Divide frequency into small bins each carrying a separate QAM
constellation
  Better use of channel capacity
  More resistance to noise
  Rate adaptability

## Slide 118: ADSL Spectrum
ADSL Spectrum is designed to:
  Allow higher download rate and lower upload rate at home
  Co-exist with telephone service
Most common mode of operation: Frequency Division Mode
  Upstream (US) 25kHz to 130 kHz providing up to 3.5 Mbps
  Downstream (DS) 140 kHz to 2.2 MHz providing up to 24 Mbps

## Slide 119: ADSL Rate
ADSL downlink and uplink rate decrease with the distance between home and local exchange

## Slide 120: Fiber To The Home (FTTH)
Fiber optic can provide a medium for providing very high speed data
services.
Bringing fiber deployment closer to the homes and businesses
facilitates the deployment of higher speed data services for end
Passive Optical Networks (PON) are becoming very popular and can run at around gigabits per second to provide different services such as
  Ethernet PONs (EPON)
  Gigabit capable PONs (GPON)

## Slide 121: FTTH Application
Faculty of EE, Sharif U of Tech
Advanced Communication Networkss
78
Source: FTTH Handbook
FTTH Council Europe

## Slide 122: Trunks and Multiplexing
TDM: time division multiplexing
(can only be used in the digital domain)
  Pulse Coded Modulation (PCM): Analog voice signals coming from local loop are sampled at 8000 samples/sec. Each sample is represented by 8 bits.
 64 kbps representation of the voice signal
  Several voice channels can be multiplexed in time to carry voice info between Telco offices.

## Slide 123: TDM carriers
N. America : T1 carrier
  1.544 Mbps
  24 x 8 + 1 = 193 bits per frame
  1 frame per 125 microseconds
  8000 x 8 = 64 kbits/second per channel
  24 analog channels
  AD-conversion: PCM 8-bit sampling
at 8000 Hz
Outside N. America : E1 carrier
  2.048 Mbps
  32 channels
  32 x 8 bits per frame
  30 data and 2 signaling channels
Higher order rates are derived from multiplexing T1 or E1 signal streams

## Slide 124: European PDH Hierarchy

## Slide 125: US PDH Hierarchy

## Slide 126: SONET/SDH
SONET (Synchronous Optical Network) and SDH (Synchronous Digital Hierarchy) are the primary standards for all types of metro and long-haul transport of traffic over fiber networks.
Design objectives:
  Unify the US, European and Japanese digital transmission systems
  Provide a multiplexing scheme or digital hierarchy
  Provide OAM support
  Direct access to low-level tributaries without the need to de-multiplex the entire
signal

## Slide 127: PDH Add/Drop
OLTU
34 - 140
8 - 34
2 - 8
OLTU
34 - 140
8 - 34
2 - 8
OLTU
34 - 140
8 - 34
2 - 8
OLTU
34 - 140
8 - 34
2 - 8
main
stand-by
140 Mbit/s
140 Mbit/s
Line Terminating Unit
Drop & Insert Station
1,2 ................. 64

## Slide 128: SDH/PDH Comparison
PDH has some disadvantages.
  Inability to identify individual channels in a higher order bit stream.
  Insufficient capacity for network management.
  There are different hierarchies in use around the world.
  Specialized interface equipment is required to inter-work the two
hierarchies.
SDH has some advantages over PDH networks.
  High transmission rates.
  Simplified add & drop function.
  Defined easy standard interconnection.
  Reliability.
  Future-proof platform for new services.

## Slide 129: SONET/SDH
SDH Rate and signaling
  155 Mbps or multiples
  270 x 9 x 8 bits per frame of 125 microseconds
SDH multiplexing
  261 x 8 x 9 bits for synchronous payload envelope (SPE)
  Payloads can carry many different types of traffic
  Header bytes are used for framing, parity, voice channels, error monitoring, IDs, clocking
and synchronization
Standards: Multiples of 4nxSTM-1
  STM-1: 155.52 Mbps
  STM-4: 622.08 Mbps
  STM-16: 2.5 Gbps
  STM-64: 10 Gbps
  STM-256: 40 Gbps

## Slide 130: SDH Network Elements

## Slide 131: SDH Add/Drop

## Slide 132: Typical Network Architecture
Communication Networkss
89
 1+1 APS
Terminal Mux
Typical Network Nodes
TM
ADM
ADM
PDH Tributaries
Terminal Mux
Linear Add/Drop Muxe
s
Dual-Ring
Add/Drop Muxes
Standard
1+1
TM
1+1
ADM
1+1
ADM
Terminal Mux
STM-1/OC-3 Link
Linear Add/Drop Muxes
CCW
CW
CCW
ADM
ADM
ADM
ADM
PDH Tributaries
PDH
Tributaries
STM-1/OC-3 RING
Linear 1+1 APS
STM-1/OC-3 Link
ADM
ADM
ADM
CW
PDH Tributaries
Ring Bridge
PDH Tributaries
PDH
Tributaries
 Linear Add/Drop Mux
 Dual Ring (UPSR) Add/Drop Mux

Terminal Mux
STM-4/OC-12 RING

## Slide 133: Switching
Communication Networkss 91
Circuit switching
  Dedicated path established between source and destination
  Long set-up time: O(10 sec)
  No congestion change: guaranteed bandwidth
  No extra random delay while call is established. Only transport delay
  Unused bandwidth is wasted
  Transparent to data format and framing mode. (road vs. railroad)

## Slide 134: Switching
Packet switching
  Store-and-forward technique used
  No dedicated path
  Packet size should be limited in order not to block switches and/or overflow buffers
  First packet is forwarded while second is received.
  Rate conversion is easy
  Delivery order may not be guaranteed

## Slide 135: Mobile Economy

## Slide 136: Mobile Economy

## Slide 137: Mobile Economy

## Slide 138: Mobile Economy

## Slide 139: Trend of Data Usage

## Slide 140: Mobile Networks

## Slide 141: Mobile Phone System
First Generation:
  Started from push to talk one to many systems (Police, Taxi’s)
  In 1960, Improved Mobile Telephone System (IMTS) was installed with
separate US and DS channels
  Had a high power transmitter with 23 channels from 150 MHz to 450MHz
  Problems with channel capacity (Low number of channels) and
interference

## Slide 142: Concept of Cellular Networks
Single hop wireless connectivity to the wired world
  Space divided into cells
  A base station is responsible to communicate with hosts in its cell
  Mobile hosts can change cells while communicating
  Hand-off occurs when a mobile host starts communicating via a new base station
Factors for determining cell size
  No. of users to be support
  Multiplexing and transmission
technologies

## Slide 143: Mobile Phone System
Advanced Mobile Phone System (AMPS) (1982)
  Divide area into radio cells to avoid interference and allow frequency re-use
  Cells are around 10 km wide
  Multiple base stations talk to a Base station switching center (BSC)
  Multiple BSC’s talk to a Mobile Switching Center (MSC) and then to the PSTN network
  832 upstream channels from 829-849 MHz, 832 downstream channels from
869-894 MHz each 30 kHz wide

## Slide 144: Mobile Phone System
Channels are used for
  Control (Base to Mobile) to
manage the system (21 channels)
  Paging (Base to Mobile) to alert
mobile users for a call
  Access (Bi-directional) for call setup and channel assignment
  Data (Bi-directional) for voice, fax and data (usually around 45 channels due to frequency re-use)
Call handling
When handset is powered on, it scans control channels to find the most powerful signal
It then broadcasts its 32 bit serial number
and phone number in digital format
BTS reports to MSC and it will decide if the
user should be accepted for service
When mobile is dialing, MSC decides upon the channel and service availability and connects the call
MSC should also handle roaming and
handoff
For incoming call, handset should continuously monitor the paging channel and respond through the control channel when a call request comes in

## Slide 145: Hand off
Hand-off necessary when mobile moves from area of one BS into another
BS initiated:
  BS monitors the signal level of the mobile
  Handoff occurs if signal level falls below threshold
  Increases load on BS
  Monitor signal level of each mobile
  Determine target BS for handoff
Mobile assisted:
  Each BS periodically transmits beacon
  Mobile, on hearing stronger beacon from a new BS, sends it a greeting
  changes routing tables to make new BS its default gateway
  sends new BS identity of the old BS
  New BS acknowledges the greeting and begins to route mobile’s call
Intersystem:
  Mobile moves across areas controlled by different MSC’s
  Handled similar to mobile assisted case with additional HLR/VLR effort

## Slide 146: Mobile Phone System - 2G
D-AMPS
  IS-54, IS-135, backward compatible with AMPS.
  Uses the same 30 kHz channels as AMPS. Therefore, D-AMPS
(Sometimes call PCS) and AMPS can coexist in the same network.
  A new band was opened for D-AMPS:
    1850-1910 MHz for US
    1930-1990 MHz for DS
  Systems with much smaller phone size and longer battery life were
developed
  D-AMPS Vocoder can compress the voice down to 8kbps or less
  Mobile Monitors the Rx quality and requests a handover to another base if there is a need

## Slide 147: Mobile Phone System - GSM
GSM: Global system for mobile communication
  Developed in Europe in 1990s
  Second generation mobile system
  Can offer voice and data

## Slide 148: Core Network
Main tasks of core network
  Call control
  Routing
  Locating
  Mobility management
  Signaling to other networks

## Slide 149: Mobile Switching Center (MSC)
Specific functions of a MSC
  Switching of 64 kbit/s channels
  Paging and call forwarding
  Termination of SS7 (signaling system no. 7)
  Mobility specific signaling
  Location registration and forwarding of location
information
  Support of short message service (SMS)
  Generation and forwarding of accounting and
billing information
Switching functions
  Additional functions for mobility support
  Interworking functions via Gateway MSC (GMSC)
 Integration of several databases

## Slide 150: Home Location Register (HLR)
Central master database that contains data from every user that has
subscribed to the operator, includes:
  Subscriber data
  IMSI - International Mobile Subscriber Identity
  List of subscribed services with parameters and restrictions
  Location data
  Current MSC/VLR address
Responsibilities of the HLR include:
  Management of service profiles
  Mapping of subscriber identities (MSISDN, IMSI)
  Supplementary service control and profile updates
  Execution of supplementary service logic e.g. incoming calls barred.
  Passing subscription records to VLR

## Slide 151: Visitor Location Register (VLR)
Local database:
  Data about all users currently in the domain of the VLR
  Includes roamers and non-roamers
  Associated to each MSC
Responsibilities of the VLR include:
  Executing supplementary service programs (outgoing calls
barred)
  Initiating authentication and ciphering
  Initiating paging
  Passing location information to HLR

## Slide 152: SMS Center (SMSC)
SMSC: stores and forwards messages to and from the SME (Short Message Entity)
On receiving the short message from the short message center, MSC uses VLR (Visitor Location Register) which contains temporary information about the mobile, (mobile identification and the cell where the mobile is currently situated)
Using information form the VLR the MSC is able to switch the information (short message) to the corresponding BSS (Base Station System, BSC + BTSs), which transmits the short message to the mobile.
If the receiving mobile is not available, the message is stored in SMSC (based on operator policies) and will be delivered when it becomes available.

## Slide 153: NSS Elements
Gateway MSC
  Connects mobile network to a fixed network
  Request routing information from the HLR and routes the connection to the local MSC
Authentication Center (AuC) (Associated to HLR)
  Supports authentication and encryption mechanisms
  Ki - subscriber secret authentication key
  A3 - authentication algorithm
  A8 - cipher key generation algorithm
Equipment Identity Register (EIR)
  Stores mobile stations IMEI (International Mobile Equipment Identity)
  White-list - mobile stations allowed to connect without restrictions
  Black-list - mobile stations locked (stolen or not type approved)
  Gray-list - mobile stations under observation for possible problems

## Slide 154: GSM Call Process
GSM Channels:
  Traffic Channels
  Signaling Channels
Signaling Channels:
  Broadcast channel for:
    Outputting identity of base station
    Each mobile checks its signal strength to
see if it has moved to another cell
  Dedicated channel for:
    Location updating
    Registration
    Call setup
  Common Control channel for:
    Paging (of incoming calls); each mobile monitors this channel
    Random access channel, using slotted Aloha to request a slot on the dedicated channel, to set up a new call
    Access grant channel
Setting up a call:
  Mobile requests a dedicated access channel# using random access channel; this is the only channel where we can get collisions; so it is used very shortly
  Base grants channel# on access grant channel
  Setup the call on dedicated channel
  Start the conversation on one of the
agreed regular channels

## Slide 155: Evolution of 2G
The demand for data connectivity in mobiles increased. Several steps were taken to define standards to support Communication Networksing in 2G networks.
General Packet Radio Service (GPRS)
  A packet oriented mobile data service on the 2G networks
  GPRS provides data rates of 56–114 kbit/second by using unused time
slots of GSM system.
  Slots are reserved for IP data traffic based on demand.
  GPRS is a best-effort service, implying variable throughput and latency that depend on the number of other users sharing the service concurrently
Enhanced Data Rate for Global Evolution (EDGE)
  EDGE is a digital mobile phone technology that allows improved data
transmission rates as a backward-compatible extension of GSM
  Peak bit-rates of up to 1 Mbit/s and typical bit-rates of 400 kbit/s can be
expected.

## Slide 156: Third Generation Mobile Systems (3G)
Initial Objectives:
  High quality voice
  High speed data for messaging, multimedia and internet access.
  Up to 2 Mbps rate to fixed users and up to 384 kbps to mobile users
Three main standards:
  Wideband CDMA
    Developed mostly in Europe
    Runs in a 5 MHz band
    Can inter-work with GSM but not backward compatible
  CDMA2000
    Developed mostly in USA
    Uses 5 MHz bandwidth
    Designed to interwork with IS-95 which is a 2G CDMA standard used in North
America
  TD-SCDMA
 Chinese version of 3G systems

## Slide 157: Evolution of Mobile Standards

## Slide 158: Long Term Evolution (LTE)
The LTE specification:
  Downlink peak rates of at least 100 Mbit/s for a single antenna, Peak download rates of 326.4 Mbit/s for 4x4 antennae, and 172.8 Mbit/s for 2x2 antennae (utilizing 20 MHz of spectrum)
  Peak upload rates of 86.4 Mbit/s for every 20 MHz of spectrum using a single antenna
  RAN round-trip times of less than 10 ms. Sub-5 ms latency for small IP packets
  Scalable carrier bandwidths, from 1.4 MHz to 20 MHz
  Five different terminal classes have been defined from a voice centric class up to a high end terminal that supports the peak data rates. All terminals will be able to process 20 MHz bandwidth
  Supports both frequency division duplexing (FDD) and time division
duplexing (TDD).
 Simpler core network architecture resulting in low operating cost

## Slide 161: Evolved Packet Core (EPC)

## Slide 162: Mobility Management Entity (MME)
The MME is an important controller node in the LTE network. It is responsible for:
  Idle mode UE (User Equipment) tracking
  Paging procedure such as re-transmissions
  Bearer activation and deactivation process
  S-GW selection for a UE at the initial attach
  Intra-LTE handover with Core Network node relocation
  User authentication with HSS

## Slide 163: Serving Gateway (SGW)
Main functions of the Serving Gateway:
  Routing and forwarding of user data packets.
  Inter-eNB handovers in the U-plane
  Mobility between LTE and other types of networks, such as between 2G/3G and P-GW.
  Replicating user traffic for lawful interception.
The DL data from the UEs in idle state is terminated at the SGW, and arrival of DL data triggers paging for the UE.
The SGW keeps context information such as parameters of the IP bearer and routing information, and stores the UE contexts when paging happens.

## Slide 164: PDN Gateway (PGW)
The PDN Gateway is the connecting node between UEs and external networks. It is the entry point of data traffic for UEs.
In order to access multiple PDNs, UEs can connect to several PGWs at the same time.
The functions of the PGW include:
  Policy enforcement
  Packet filtering
  Charging support
  Lawful interception
  Packet screening
  Mobility between 3GPP and non-3GPP networks

## Slide 165: EPC Protocol Stacks: Signaling

## Slide 166: EPC Protocol Stacks: Data Plane

## Slide 167: More Detailed EPC

## Slide 168: Evolution to 5G

## Slide 169: Evolution to 5G

## Slide 170: Evolution towards 5G

## Slide 171: Mobile Technology Trend
Source:

## Slide 172: Mobile Technology Trend
Source:

## Slide 173: Data Communication Networks Data Link Layer
Communication Networkss
1
DR.Eslami
Department of ElectricalEngineering
Islamic Azad University،Science And Research Branch

## Slide 174: Data link layer
Data Link Layer Purpose:
  Ensure reliable, efficient communication between neighbor nodes
Four specific functions:
  Provide services to network layer
  Framing
  Error handling
  Flow control
Overview
  Design issues
  Error detection and correction
  Elementary protocols
  Sliding window protocols
  Example protocols

## Slide 175: Data Link Layer
Operation Perspective

## Slide 176: Data Link Layer
Communication Networkss
Data Link operation in a network

## Slide 177: Services Provided to Network Layer
Services provided to Network Layer:
  Unacknowledged Connectionless
  Acknowledged Connectionless
  Acknowledged connection oriented

## Slide 178: Services Provided to Network Layer
Unacknowledged connectionless
  Just send frames towards the destination
  No connection is established, No connection released
  No acknowledge of received frames
  No attempt to recover lost frames
Appropriate in case of:
  Real-time traffic: speech, video: Short delay more important than 100% reliability
  Low error channels: leave error correction to higher layers
  Most LAN’s are using this service class
Example: Ethernet

## Slide 179: Service to Network Layer
Acknowledged connectionless
  Each frame is acknowledged, but no connection is established
  Acknowledgment is a service that can be performed by the transport layer as well
  Data link layer provides this service to avoid long delays
that could be caused if frames are not acknowledged
  Specially important over un-reliable channels such as wireless
Example: 802.11 (WiFi)

## Slide 180: Service to Network Layer
Acknowledged Connection Oriented
  Establishes a connection before sending data
  Each frame is numbered
  Data link layer guarantees the delivery of a SINGLE copy of EVERY frame (With acknowledged connectionless, it is possible to receive multiple copies of a frame due to a lost ACK)
  Releases the connection at the end of conversation (To release software and hardware resources tied up to the connection)
  Provides a reliable bit stream to NL

## Slide 181: Framing
Character stuffing
  Insert ASCII known characters to specify boundaries (FLAG)
  Insert ESC before accidental FLAGs or ESCs of binary files. To be
removed by the receiver’s data link layer
  Choice of marking characters (ESC, FLAG) Depends on 8 bit ASCII character set

## Slide 182: Framing
Bit Stuffing
  Use a flag bit pattern (01111110)
  Stuff a zero after 5 1’s if it happened in user data
  Easy to recover the frame if sync is lost

## Slide 183: Framing
Coding Violation
  Send physical layer signals that can not be associated with valid data sets to indicate frame boundaries
Example: 4B/5B coding
  Groups of 4 bits are mapped into group of 4 bits such that there is at least two transitions per block of bits
  Special codes that are not part of the normal pattern (coding violations) can determine start and end of frames.
    Start Delimeter: 11000 10001
    End Delimeter: 01101 00111
Data (Hex) | Data (Binary) | 4B5B Code
0 | 0000 | 11110
1 | 0001 | 01001
2 | 0010 | 10100
3 | 0011 | 10101
4 | 0100 | 01010
5 | 0101 | 01011
6 | 0110 | 01110
7 | 0111 | 01111
8 | 1000 | 10010
9 | 1001 | 10011
A | 1010 | 10110
B | 1011 | 10111
C | 1100 | 11010
D | 1101 | 11011
E | 1110 | 11100
F | 1111 | 11101

## Slide 184: Error Detection and Correction
Error handling
  Errors usually occur in bursts
  Advantage: fewer frames are corrupted
  Disadvantage: burst errors harder to detect and correct
Two approaches:
  Detection
  Correction
Both require extra bits per data word or message
Idea: add r extra bits to frame data
Not all 2m+r codes are legal (only 2m codes are legal)
n = m + r bits code word, m bits for data and r bits added for error
control

## Slide 185: Error Control Coding
Noise and other imperfections can cause errors in symbol detection

## Slide 186: Error Control Coding
Error control codes can be used to reduce the chance of error.

## Slide 187: Error Control Coding
Detection of errors caused by noise or other impairments during transmission from the transmitter to the receiver.
Error Detection
Detection of errors and reconstruction of the original, error-free data
Error Correction

## Slide 188: Error Control Coding
Idea: Add controlled redundancy to the message
m
Linear Encoder
m
r
n=m+r
m
Convolutional
Encoder
n=m+r

## Slide 189: Hamming Distance
The Hamming distance (HD) of 2 code words a and b is the number of bit positions in which a and b are different:
HD (a,b)= Number of ones in (a XOR b)
Note that HD (a,b) bit errors are required to convert a into b (or vice
versa )

## Slide 190: Error Detection Codes
To guarantee the detection of up to s errors in all cases, the minimum Hamming distance in a block code must be 𝑑𝑚𝑖𝑛 = 𝑠 + 1

## Slide 191: Error Control Coding
Example 1: parity
  Add (parity) bit to every data word such that total numbers of ones is even (or odd)
    HDmin = 2
    Single bit errors are detectable

## Slide 192: Error Correction Codes
To guarantee correction of up to t errors in all cases, the minimum Hamming distance in a block code must be 𝑑𝑚𝑖𝑛 = 2𝑡 + 1

## Slide 193: Error Control Coding
Example 2:
  4 data words with HDmin = 5
  If 00000.00111 arrives, what is the original?
Input | Encoded Output
00 | 00000.00000
01 | 00000.11111
10 | 11111.00000
11 | 11111.11111

## Slide 194: Error Control Coding
How many redundant (r) bits do we need for a single bit error correction?
  Assume m bit message with r bits added for single error correction (n = m+r bits)
  How many legal code-words? 2m
  How many illegal codes per code-words? n*(2m)
  (n+1)*(2m)<2n => (m+r+1)<2r
  This is the minimum number of bits (r) we need to correct a single error in n bits with r parity bits
Example: M=8 => r>=4
; M=16 => r>=5 ; M=240 => r>=8

## Slide 195: Error Control Coding
Error Detection
Encoder adds overhead for error detection
Decoder detects error and requests re-transmission in case of error (Automatic Repeat request (ARQ))
Forward Error Correction (FEC)
Encoder adds overhead to enable correction at the decoder
Avoids delay of ARQ
More overhead and increased complexity
Hybrid ARQ
Send messages with FEC and if decoding was not successful, request re-
transmission
Send messages with error detectioin codes and if there was an error, request FEC from source

## Slide 196: Error Control Coding
In some scenarios, error detection with retransmission is more efficient than error correction
Example:
  Error rate 10-6 ---- Block size 1000 bits
  Single bit error correcting requires 10 bits / block
  Single bit error detection requires 1 bit / block
  Retransmission of 1 block (= 1001 bits) per 1000 blocks is more efficient

## Slide 197: Burst Errors
In many scenarios, errors are seen as burst of errors
FEC codes allow correction of a limited number of errors per block
Burst errors may prevent decoders from recovering the correct message

## Slide 198: Interleaving
We modify the order of symbol transmission at the source and re-order them at the receiver to allow proper operation of FEC

## Slide 199: Interleaving

## Slide 200: Interleaving

## Slide 201: Cyclic Redundancy Check (CRC)
Redundancy added to a block of bytes that uses cyclic codes to check and verify the block.
Some standardized CRCs
Name | Length of CRC | Example Application
CRC-8 | 8 | DVB-S2
CRC-16 | 16 | Bluetooth
CRC-32 | 32 | Ethernet

## Slide 202: Elementary DL Protocols
Assumptions:
  Send a long data stream from sender to receiver
  Checksum errors are signaled
by the physical layer
  NL, DL, PL are independent processes
  Connection-oriented, reliable service needed at NL => one and only one copy of each frame and in the exact sequence should be received by NL

## Slide 203: Data Link: Flow Control
Data Link layer protocol runs on two different systems with possibly different hardware/software characteristics.
If the sender sends its frame at rate 𝑅𝑎 and the receiver can process only at rate 𝑅𝑏 where 𝑅𝑎 > 𝑅𝑏, then the receiver will be overloaded and unable to receive all frames correctly.
Therefore, we need to have a flow control mechanism in data link layer
The solution: Use Acknowledgment

## Slide 204: We Need “ACK”
Node A waits for an Ack frame from Node B before sending its next frame
Frame Length in Time: 𝑇𝑓 =
𝑁𝑓 (𝑓𝑟𝑎𝑚𝑒 𝑙𝑒𝑛𝑔𝑡ℎ 𝑖𝑛 𝑏𝑖𝑡𝑠)
𝐴
𝑅 (𝑇𝑟𝑎𝑛𝑠𝑚𝑖𝑡 𝑅𝑎𝑡𝑒 𝑜𝑓 𝐴)

𝐿 (𝐷𝑖𝑠𝑡𝑎𝑛𝑐𝑒 𝑏𝑒𝑡𝑤𝑒𝑒𝑛 𝑡𝑤𝑜 𝑛𝑜𝑑𝑒𝑠)
Propagation Delay: 𝑇𝑝 = 𝑉 (𝑠𝑝𝑒𝑒𝑑 𝑜𝑓 𝑠𝑖𝑔𝑛𝑎𝑙 𝑝𝑟𝑜𝑝𝑎𝑔𝑎𝑡𝑖𝑜𝑛)
A
B
t
t
B receives the frame and then generates an Ack
Tf Tp Tp

## Slide 205: We Need “Timers”
What if a frame is not received correctly?
  A could wait for the Ack that B has not transmitted (Mutual Locking)
  Solution: A should have a timer to re-send to lost frame after some time
A
B
t
t
B: Frame Error or no Frames Received
Tf
Ttime-out
Tp

## Slide 206: We Need “Frame Number”
1
1
A
B
t
t
B receives the frame correctly, but the Ack is lost
What if the Ack is lost?
  A sends the same frame again. Therefore, data link layer in B has two of the same frame. (Frame duplication)
  Solution: We need to use frame numbers to avoid duplication
Ttime-out
Tf Tp Tp

## Slide 207: We Need “Ack Number”
What if the Timers are not set properly?
  A receives an Ack after frame#1, so it thinks that frame #1 is delivered correctly to B, but this may not be true!
  Solution: We should use Ack Numbers so A knows which frame was Acked.

## Slide 208: Stop and Wait Protocol
A (TX) sends its numbered frames, starts a timer for each frame and waits for an Ack for that exact same frame
B (RX) checks the received frame and sends a Numbered Ack to
confirm.
A (TX) Stops and Waits for the correct Ack before it continues to the next frame
Seq# | Ack# | Packet | CRC
Frame

## Slide 209: Stop and Wait
If 𝑎 = 𝑇𝑝/𝑇𝑓 is not very small, then stop and wait is inefficient.
A
B
t
t
Tf
Tp
Tp
Tf
Tp
Tp
Tf
Tp
Tp

## Slide 210: Go Back N
Stop and Wait is inefficient when propagation delay is larger than the packet transmission time – Can only send one packet per round- trip time
Go Back N allows transmission of new packets before earlier ones
are acknowledged
Go back N uses a window mechanism where the sender can send packets that are within a “window” (range) of packets – The window advances as acknowledgements for earlier packets are received

## Slide 211: Go Back N
Window size = N
Sender cannot send packet i+N until it has received the ACK for packet i
Receiver operates just like in Stop and Wait
  Receive packets in order
  Receiver cannot accept packet out of sequence
  Send RN = i + 1 => ACK for all packets up to and including i
Use of piggybacking
  When traffic is bi-directional RN’s are piggybacked on packets going in the other direction
  Each packet contains a SN field indicating that packet’s sequence
number and a RN field acknowledging packets in the other direction

## Slide 212: Go Back N
The transmitter has a "window" of N packets that can be sent without acknowledgements
This window ranges from the last value of RN obtained from the receiver (denoted SNmin) to SNmin+N-1
When the transmitter reaches the end of its window, or times out, it goes back and retransmits packet SNmin
Let SNmin be the smallest number packet not yet ACKed
Let SNmax be the number of the next packet to be accepted from the higher
layer (I.e., the next new packet to be transmitted)

## Slide 213: Go Back N
Sender:
  k-bit seq # in frame header
  “window” of up to N, consecutive unACK’ed frames allowed
  ACK(n): ACKs all frames up to, including seq # n - “cumulative ACK”
  may receive duplicate ACKs (see receiver)
  timer for each in-flight frames
  timeout(n): retransmit frames n and all higher seq # frames in window

## Slide 214: Go Back N – Sender Algorithm
SNmin = 0; SNmax = 0
Repeat
  If SNmax < SNmin + N (entire window not yet sent)
    Send packet SNmax ;
    SNmax = SNmax + 1;
  If packet arrives from receiver with RN > SNmin
    SNmin = RN;
  If SNmin < SNmax (there are still some unacknowledged packets) and sender cannot send any new packets
    Choose some packet between SNmin and SNmax and re-send it or do not send anything
The last rule says that when you cannot send any new packets you should re-send an old (not yet ACKed) packet
There may be two reasons for not being able to send a new packet
  Nothing new from higher layer
  Window expired (SNmax = SNmin + N )
No set rule on which packet to re-send
  Least recently sent

## Slide 215: Go Back N – Receiver Algorithm
RN = 0;
Repeat
  When a good packet arrives,
    if SN = RN
      Accept packet
      Increment RN = RN +1
At regular intervals send an ACK packet with RN
  Most implementations send an ACK whenever they receive a packet from the other direction
  ACK can be delayed for piggybacking
Receiver reject all packets with SN not equal RN
  However, those packets may still contain useful RN numbers
Note that packet RN-1 must be accepted at B before a frame containing request RN can start transmission at B

## Slide 216: Notes of Go Back N
Requires no buffering of packets at the receiver
Sender must buffer up to N packets while waiting for their ACK
Sender must re-send entire window in the event of an error
Receiver can only accept packets in order
  Receiver must deliver packets in order to higher layer
  Cannot accept packet i+1 before packet i
  This removes the need for buffering
  This introduces the need to re-send the entire window upon error
The major problem with Go Back N is this need to re-send the entire window when an error occurs.
This is due to the fact that the receiver can only accept packets in
order

## Slide 217: Go Back N Counters
B
Window Size: N
Sequence Counter: M different numbers (For example, If the counter has 3 bits, M=23=8)
A
t
t
7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
A
B
t
t
7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7

## Slide 218: Go Back N Counters
Window Size: N
Sequence Counter: M different numbers (For example, If the counter has 3 bits, M=23=8)
We should always choose N<M
A
t
t
6
0 | 1 | 2 | 3 | 4 | 5 | 6
5
7 | 0 | 1 | 2 | 3 | 4 | 5
B
A
t
t
6
0 | 1 | 2 | 3 | 4 | 5 | 6
6
7 | 0 | 1 | 2 | 3 | 4 | 5
B
B
B

## Slide 219: Selective Repeat
Selective Repeat attempts to retransmit only those packets that are actually lost (due to errors)
  Receiver must be able to accept packets out of order
  Since receiver must release packets to higher layer in order, the
receiver must be able to buffer some packets
A
B
fr 0
time
fr fr
1 2
fr fr fr
3 4 5
fr 6
fr fr fr fr
2 7 8 9
fr fr fr
10 11 12
A C K | A C K | N A K | A C K | A C K | A C K | A C K | A C K | A C K | A C K | A C K | A C K
1 2 error 2 |  |  | 2 | 2 | 2 | 7 | 8 | 9 | 1 | 1 | 1
 |  |  |  |  |  |  |  |  | 0 | 1 | 2

## Slide 220: Selective Repeat
Retransmission requests
  Implicit
    The receiver acknowledges every good packet, packets that are not
ACKed before a time-out are assumed lost or in error
    Notice that this approach must be used to be sure that every packet is eventually received
  Explicit An explicit NAK (selective reject)
    can request retransmission of just one packet
    This approach can expedite the retransmission but is not strictly needed
  One or both approaches are used in practice

## Slide 221: Selective Repeat

## Slide 222: Selective Repeat

## Slide 223: Selective Repeat Example
Communication Networkss
RR3 means the receiver has received all frames up to frame 2 and is ready to receive frame 3.
Have been delivered to upper layer
More spaces for future frames

## Slide 224: Selective Repeat Algorithm
Sender:
  Can transmit new packets as long as their number is within W (Window Size) of all un-
ACKed packets
  Retransmits un-ACKed packets after a timeout (Or upon a NAK if NAK is employed)
  Must buffer all packets until they are ACKed (Up to W un-ACKed packets are possible)
Receiver:
  ACKs all correct packets
  Stores correct packets until they can be delivered in order to the higher layer
  Must buffer packets until they can be delivered in order i.e., until all lower numbered packets have been received. This is needed for orderly delivery of packets to the higher layer
  Up to W packets may have to be buffered (in case the first packet of a window is lost)
Implication of window size = N
  Number of un-ACKed packets at sender =< N (window limit at sender)
  Number of un-ACKed packets at sender cannot differ by more than N (window limit at
the receiver required to deliver packets in order)
  Packets must be numbered modulo M >= 2N (using log2(M) bits)

## Slide 225: Selective Repeat Counters
B
Example: Window Size N=4
Case 1) Frame#0 has error, therefore B send NAK#0 and A sends frame#0 after frame#3
Case 2) A sends frame#3, frame#4, frame#5, frame#6 and frame#7. All frames between frame#3 and frame#7 are lost. Therefore, B receives frame#3 followed by frame#7
We should have a numbering system that allows differentiation between these two cases
A
t
t
NAK 0
0 | 1 | 2 | 3 | 0
A
t
3 | 4 | 5 | 6 | 7
1
B
ACK 3
t
7
Communication Networkss
3
2
3
0

## Slide 226: Selective Repeat Counters
B
In general, the range of packets that may follow packet i at the receiver (Ex: N=4, Set i=3)
Packet i may be followed by the first packet of the window (i -N+1) if it requires retransmission
Packet i may be followed by the last packet of the window (i+N) if all Of the frames between i and i
+N are lost
Receiver must differentiate between packets i -N+1 ... i +N
These 2N packets can be differentiated using Mod 2N numbering
In Selective Repeat, we should choose M2N
A
t
t
NAK 0
0 | 1 | 2 | 3 | 0
A
t
3 | 4 | 5 | 6 | 7
1
B
ACK 3
t
7
Communication Networkss
3
2
3
0

## Slide 227: Performance Analysis of L2 Protocols

## Slide 228: Performance Analysis of L2 Protocols

## Slide 229: Link Utilization
ata Networks 57
Error Free Operation
Stop and Wait:

W  2a 1
2a 1
W
Sliding Window (W=window Size=2n-1):
1 W  2a 1
U  
2a 1
1
U 
frame
D
T
a  Tprop

## Slide 230: Link Utilization
Probability of frame error = p
Stop and Wait Utilization
  Probability of a frame requiring exactly k transmission = pk-1(1-p)
  Expected Number of Transmission for a frame (Nr):
Utilization should be divided by Nr :
Selective Reject Utilization
  Exact same idea as stop and wait
k 1
k 1
1 p
 
 k  Prob(k Transmission) kpk 1 (1 p)  1
r
E[N ]  N
1 2a
U  1 p


1 p W  2a 1
W  2a 1
U  W (1 p)
 1 2a

## Slide 231: Link Utilization
Go back N Utilization
  Each frame error requires re-transmission of L packets where L1
  Total number of frames that should be transmitted if the original frame
must be transmitted k times=f(k)=1+(k-1)L


W  1 2a
W W  1 2a
L  1 2a
1 p 1 p
k 1 k 1
 (1 L) pk 1 (1 p)  Lkpk 1 (1 p)  (1 L)  L  1 p  LP
 
r
 
E[N ]  N   f (k)  Prob(k Transmission) (1 L  kL) pk 1 (1 p)
k 1 k 1



(2a 1)(1 p  Wp )

U 
W  2a 1
1 2ap W (1 p)
W  2a 1
1 p

## Slide 232: Link Utilization

## Slide 233: HDLC
Primary | Commands | Secondary
 | Responses | 
Unbalanced Point-to-point link
Primary
Commands
Responses
Secondary
Secondary
Secondary
Unbalanced Multipoint link
Primary | Commands Responses | Secondary
Secondary | Responses Commands | Primary
Balanced Point-to-point link between Combined Stations
HDLC: high-level data link control
  Common in X.25 networks
  Derived from IBM’s SNA
  Bit-oriented, bit-stuffing
Station Types:
  Primary station
    Controls operation of link
    Frames issued are called commands
    Maintains separate logical link to each
secondary station
  Secondary station
    Under control of primary station
    Frames issued called responses
  Combined station
    May issue commands and responses

## Slide 234: HDLC
Primary | Commands | Secondary
 | Responses | 
Unbalanced Point-to-point link
Primary
Commands
Responses
Secondary
Secondary
Secondary
Unbalanced Multipoint link
Primary | Commands Responses | Secondary
Secondary | Responses Commands | Primary
Balanced Point-to-point link between Combined Stations
HDLC Link Configurations (Full duplex & Half duplex)
  Unbalanced: One primary and one or more secondary stations
  Balanced: Two combined stations
Normal Response Mode (NRM)
  Unbalanced configuration
  Primary initiates transfer to secondary. Secondary may only transmit data in response to command from primary
  Used on multi-drop lines
  Host computer as primary.
  Terminals as secondary
Asynchronous Balanced Mode (ABM)
  Balanced configuration (Most widely used)
  Either station may initiate transmission
without receiving permission. No polling overhead

## Slide 235: HDLC
Frame Structure
  All transmissions in frames
  Single frame format for all data and control exchanges
  On idle point to point links, flag sequences are transmitted continuously
Flag Fields
  Delimit frame at both ends with 01111110
  May close one frame and open another
  Receiver hunts for flag sequence to synchronize
  Bit stuffing used to avoid confusion with data containing 01111110
    0 inserted after every sequence of five 1s
    If receiver detects five 1s it checks next bit
    If 0, it is deleted
    If 1 and seventh bit is 0, accept as flag
    If sixth and seventh bits 1, sender is indicating abort

## Slide 236: HDLC Frame Fields
Address Field
  Identifies secondary station that sent or will receive frame
  Usually 8 bits long
  May be extended to multiples of 7 bits
    LSB of each octet indicates that it is the last octet (1) or not (0)
  All ones (11111111) is for broadcast

## Slide 237: HDLC Control Field
Control frame varies for different frame types
  Information - data to be transmitted to user (next layer up)
    Flow and error control piggybacked on information frames
  Supervisory - ARQ when piggyback not used
  Unnumbered - supplementary link control
First one or two bits of control field: frame type identification

## Slide 238: HDLC frame types
Supervisory frames
  Receive Ready Frame (SS=00)
    Used when there are no information frames available to piggyback the ACK
  Reject Frame (SS=01)
    Receiver tells the sender to go back and start sending from the frame number N(R)
  Receive Not Ready (SS=10)
    All frames up to frame number N(R) have been received properly. But the receiver can not accept any frames at this time. (e.g. due to a full buffer)
  Selective Reject (SS=11)
    Receiver asks the sender to re- send frame number N(R)
Unnumbered frames
Used to start up the link or tear it down
Some examples:
  SABM: Set ABM Mode
  SNRM: Set NRM Mode
  SABME: Set ABM Extended Mode
  DISC: Disconnect
  UA: Unnumbered Acknowledgment
  FRMR: Frame Reject

## Slide 239: PPP - Point-to-Point Protocol
Provides a method for encapsulation of network layer packets over point to
point links. It provides:
  An HDLC-like Framing with error detection (Byte oriented)
  LCP (link control protocol) for bringing up lines, testing, negotiating options
  NCP (network control protocol) for each supported network layer
PPP frame format
  Flag byte: 0111.1110 / character stuffing
  Address field (default = 1111.1111)
  Control field (default = 0000.0011)
  Unnumbered frames with unreliable transmission; no sequence numbers
  Protocol field: indicates packet type
    0x indicates IP, IPX or XNS
    1x indicates LCP, NCP or others
  Payload: 1500 bytes default length
  Checksum of 2 (default) or 4 bytes

## Slide 240: Typical PPP Operation
Example 1: Home PC to Internet Service Provider
  PC calls router via modem.
  PC and router exchange LCP packets to negotiate PPP parameters.
  Check on identities.
  NCP packets exchanged to configure the network layer, e.g., TCP/IP (requires IP address assignment).
  Data transport, e.g. send/receive IP packets.
  NCP used to tear down the network layer connection (free up IP address); LCP used to shut down data link layer connection.
  Modem hangs up.
Example 2: PPP use for transmission of
packets over SONET SDH links

## Slide 241: Data link layer in ATM
There are no physical layer characteristics specific to ATM
  ATM cells can be carried by various physical layer services such as SONET/SDH, ADSL or wireless links
TC (transmission convergence) sub layer corresponds to DL layer
Transmission: each cell of 53 byte includes 5 byte header
  Add 4 bytes of identification and 1 byte of HEC (header checksum)
  No checksum for payload. (BER<< 10-12 in fiber optic links)
  Match speed to underlying physical transmission system by inserting empty or
maintenance (OAM) cells
Reception of a cell
  Locate cell boundaries
  Verify header
  Discard cells with invalid headers
  Process maintenance cells
  Pass data to ATM layer

## Slide 242: Data link layer in ATM
How to detect cell boundaries (there are no marks !!)
  Trick: constantly check HEC field after each incoming bit
  Use 40-bits shift register to shift the incoming pattern bit-by-bit until the frame header is found
  After the first header match, jump 53 bytes (length of an ATM frame) and re-
check the HEC (is this the right HEC for the assumed cell?)
  Repeat the header check d times in a row, If all correct, go to synch Mode
  Change of accidental correct synchronization = 2-8d
  ‘DeSynch’ after a incorrect headers
  TC sub layer uses header of ATM field for synchronization: no proper separation
of layers. E.g. changing header format for ATM affects TC layer

## Slide 243: Data Communication Networks Multiple Access Control Sublayer
DR.Eslami
Department of Electrical Engineering
Islamic Azad University،Science And Research Branch

## Slide 244: The Medium Access Sublayer
A number of systems are connected to share the medium: Who gets access?
  Used for LANs
  Addressing
  Broadcast
1
2
3
4
5
M
Shared Multiple Access Medium


## Slide 245: Network Protocol Design Goals
Static
user gets a channel for the whole ‘conversation’.
Dynamic
Channel capacity allocated for a user is not fixed; depends on usage.

## Slide 246: Static Channel Allocation
Using FDM or TDM to divide channel capacity among N users
Inefficient bandwidth use: some users may be idle
Users may be denied access even when other users do not use there allocated capacity
Long time service delay T

## Slide 247: Static Channel Allocation
Delay in a single M/M/1 Queue
  Channel can transfer C bits/sec
  Frames arrive randomly with an average rate of  frames/sec and the inter-arrival times are exponentially distributed
  Frame length values has an exponential distribution with an average length of 1/
bits.
Mean delay of frames in the queue is given by:𝑇 = 1
𝜇𝐶−𝜆
Example: C=100 Mbps, 1/=10000 bits, =5000 frames/sec, T=200 sec

## Slide 248: Static Channel Allocation
Delay if we divide the channel into N sections
  Assume we divide the same stream into N smaller streams and serve each of them in a separate queue
  There will be N channels with a capacity of C/N bits/sec for each
  There will be N streams with an average rate of /N frames/sec each
1 𝑁
Mean delay of each queue: 𝑇𝑁 = 𝐶 𝜆 = = 𝑁𝑇
𝜇 − 𝜇𝐶−𝜆
𝑁 𝑁
Example: If we divide the above queue into 4 sections, 𝑇𝑁 = 800 𝜇𝑠𝑒𝑐

## Slide 249: Dynamic Channel Allocation
In data communication, the peak to mean ratio of traffic can be very high.
In many applications, users require the channel in random
times
Static allocation will be a waste of channel resources
It is best to assign the channel based on user demand
Different protocols for coordination:
  ALOHA : pure and slotted
  CSMA : carrier sense multiple access protocols
  Ethernet
  Wireless LAN protocols

## Slide 250: Dynamic Channel Allocation
Assumptions for analysis of dynamic channel allocation algorithms:
  Station model:
    N independent stations generating frames within interval t with
probability =  t where  is frame rate (frames/second)
  Single communication channel
  Collision occurs when 2 frames are transmitted simultaneously
  Time is
    a) continuous, or
    b) slotted (discrete intervals)
  Stations may have the hardware to notice:
    Collision of frames
    The presence of another signal on the channel (carrier sense)

## Slide 251: Multiple Access Protocols
ALOHA:
  Station transmits as soon as it has a frame
  If a collision is detected, it waits for a random time interval and
then retransmits

## Slide 252: ALOHA Efficiency
Notes and assumptions:
  Large number of stations
  Frames of equal length
  Transmit time for frame on the channel is normalized to unity
  Stations can sense channel collision and re-try transmission if there is a collision
Poisson distribution:
  Poisson distribution is drived from the binomial distribution:
  If event happens with probability p, the probability that the event happens exactly
X times in N trials is:
 X 
P( X )    p X (1 p)N  X
 N 
If N is large and p is not close to 0 or 1 we get a Normal distribution
If N is large and p is small (rare event) we get a Poisson distribution
Probability of k events in a given time interval:
k!
GkeG
Pr [k] 

## Slide 253: System Model
Frames are buffered at MAC
MAC controls transmission of frames on the channel
Channel
PHY
MAC
Upper Layer
PHY
MAC
Upper Layer
PHY
MAC
Upper Layer
PHY
MAC
Upper Layer

## Slide 254: ALOHA Efficiency
Analysis:
  All stations together, generate an average of S new frames per frame time
    If S>1, every frame suffers a collision, so for reasonable operation, 0<S<1
    A station does not send a new frame until the old frame has been transmitted successfully. So, S can be seen as a measure of throughput as well.
  Probability of k attempts per frame time by all stations, old and new combined is Poisson with mean G per frame time.
  Low load rare collision  SG
  Increase the load  More collisions  G>S
  Throughput is then the offered load, G, times the probability of no collision, P0
 S=GP0

## Slide 255: ALOHA Efficiency
Probability of k frames generated per frame-time (t) is (Poisson distribution)
Probability that there is no frame
generated in a given interval t is
r
No collision if no other frame
generated in two frame-times.
Mean number of frames generated during 2t sec is 2G so:
ALOHA Efficiency:
k!
GkeG
Pr [k] 
P [0]  eG
k!
2G
(2G)k e2G
Pr[k]   Pr[0]  e
S  Ge2G

## Slide 256: Slotted ALOHA Efficiency
Divide time in discrete intervals
Users have to agree on slot
boundaries
In each slot, one or more users send their frames
Probability of transmission success (no other frame is generated in a given interval) t is
G
k!
(G)k eG
Pr[k]   Pr[0]  e
Slotted ALOHA Efficiency:
S  GeG
Maximum channel utilization:
  Pure Aloha : 18.4%
  Slotted Aloha : 36.8% (37% empty slots, 26% collisions)

## Slide 257: Impact of Load
Probability of transmission failure for a single frame in slotted ALOHA:
P  (1 eG )
Probability of a transmission requiring exactly k attempts:
Expected Number of transmissions per frame is:
For ALOHA, with the same analysis, E=e2G
A small increase in channel load, G can results in exponentially increase in transmissions (most of which cause collisions) resulting:
  Reduced system throughput (S)
  Longer queues in MAC layer for accumulated, waiting frames.
  Increase in average frame delay
 
E 
G
G G k 1
 k 
k 1 k 1
kP  ke (1 e )  e
k
P  eG (1 eG )k1

## Slide 258: Delay Analysis
Frame transmission duration: X
Frame propagation time: tprop
Average back-off time: B
Average number of transmission attempts per frame (ALOHA): G/S=e2G
Average number of unsuccessful attempts per frame: =G/S-1=e2G-1
Successful transmission requires X+tprop seconds and each re-transmission requires 2tprop+X+B seconds
Therefore, average MAC delay in ALOHA is given by:
E[TALOHA]=X+tprop+(e2G-1)(X+2tprop+B)
Normally, back-off time is uniformly distributed between 1 and K packet transmission times and therefore, B=(K+1)X/2
For Slotted ALOHA, the MAC delay is given by:
E[TALOHA]=X+tprop+(eG-1)(X+2tprop+B)

## Slide 259: MAC Layer trade offs
Data Networ
ks 17
Normalized Transfer Delay (NTD):
  A measure of delay caused
by access control algorithm (Collisions, reservations, etc).
Normalized Delay Bandwidth (a):
  Number of lost frames due to a collision is proportional to a
Example: 1000 bit frames, 2 Mbps channel, 40 msec. one-way delay 
For ALOHA type MACs, the trend is:
  When Load is low, NTD is near 1.
NTD increases steadily as load is increased.
Maximum achievable load is usually much less than 1.
Maximum achievable load decreases when a is increased ( Cost of MAC is higher for long distance or high speed links)
Normalized Transfer Delay
Load
E[T]/E[X]

max
1
1
max
a
a′
a′ > a
NTD  E[T ]  (Average TransferDelay)
E[X ]  (Average FrameTransmission Time)
Average FrameSize
a  One waydelay Bandwidth
 80
1000
2106  40103
a 

## Slide 260: Carrier Sense Multiple Access Protocols (CSMA)
Idea: The number of collisions can be reduced by sensing the carrier before transmission
1-persistent
  Listen to channel and transmit as soon as channel becomes idle
  If collision, wait random time, and try again

## Slide 261: CSMA Protocols
Non-persistent:
  Sense channel; if idle, transmit. If not idle, wait a random period before sensing the channel
  Better utilisation, however, longer delays

## Slide 262: CSMA Protocols
P-persistent:
  Sense channel, if idle, transmit with probability p, defer With probability 1-p to the next slot.
  If next slot idle repeat the same algorithm
  If busy the first time, wait till next time slot and try again

## Slide 263: Throughput of ALOHA and CSMA

## Slide 264: CSMA with Collision Detection
Widely used on LANs in MAC sublayer (IEEE 802.3; Ethernet)
Idea: stop directly after detecting collision and wait for a random period

## Slide 265: CSMA with Collision Detection

## Slide 266: CSMA with Collision Detection
How long does it take to detect collision?
  Assuming a max travel time of tprop, it takes 2tprop to be sure (contention period) (10 sec on 1 km cable)
A transmits at t = 0
Distance d meters
tprop = d / ν seconds
A
B
B transmits before t = tprop and detects collision shortly thereafter
A
B
A
B
A detects collision at t = 2 tprop

## Slide 267: CSMA with Collision Detection
Although CSMA/CD avoids collisions once a station has seized the channel; collisions still occurs during the contention period
Contention period may become large for long (fibre) cables

## Slide 268: Token Passing
Some MAC protocols rely on token.
The token represents permission to send
If a station has a frame queued for transmission when it receives the token, it can send that frame before it passes the token to the next station.
If it has no queued frame, it simply passes the token.
In a token ring protocol, the topology of the network is used to define the order in which stations send.
Token passing can also be used in a bus mode where stations pass token to each other in a predefined order.
Examples:
  Token Ring
  Token Bus
  FDDI
  RPR

## Slide 269: IEEE 802 standards
IEEE 802 refers to a family of IEEE standards dealing with local area networks and metropolitan area networks:
  IEEE 802: Overview & Architecture
  IEEE 802.1 Bridging & Management
  IEEE 802.2: Logical Link Control
  IEEE 802.3: CSMA/CD Access Method (Ethernet)
  IEEE 802.5: Token Ring Access Method
  IEEE 802.11: Wireless Local Area Networks (LAN)
  IEEE 802.15: Wireless Personal Area Networks (PAN)
  IEEE 802.16: Broadband Wireless Metropolitan Area Networks (MAN)
  IEEE 802.17: Resilient Packet Rings (RPR)
  IEEE 802.20: Mobile Broadband Wireless Access
  IEEE 802.21: Media Independent Handoff
  IEEE 802.22: Wireless Regional Area Network
  IEEE 802.23: Emergency Services Working Group

## Slide 270: Ethernet
Original design for 1-10 Mbps
Various media, first used on 50 ohm coaxial cable
Started as ALOHA system on Hawaiian Islands
Carrier sensing was added by Xerox

## Slide 271: Ethernet Topology

## Slide 272: Ethernet Topology

## Slide 273: Ethernet Reference Model

## Slide 274: 802.3 Frame Structure
Preamble: 7 x 1010.1010 pattern
  Creates 10 MHz square wave of 5.6 microsecond for synchronization
Start field: 1010.1011 denotes start of frame

## Slide 275: 802.3 Framing
Length field: 0-1500 bytes
Data: payload
Ethernet frames should be long enough to allow collision detection at the source. Therefore, a Pad field is defined to extend the length of short frames.
Pad: ensure minimum frame length = 64 bytes.

## Slide 276: 802.3 Pad Field
LAN Length (L) = 500 m (per segment) x 5 segments = 2500 meters
Velocity of propagation on the cable (V) = 2 * 108 meters/sec
Delay added by repeater (D) = ~3uSec x 2 (Bi-Direction) x 4 Repeaters = 24uSec
Round Trip Delay (RTD) = (Total Distance/V) + Repeater Delays (D) Total Distance/V = (2*2500/2 * 108) = 25 * 10-6 sec or 25usec Hence RTD = 25 + 24 = 49 usec
Now, time to transmit 64 bytes = 512 bits / 10 * 106 = 51.2 10-6 sec or 51.2 usec (referred to as slot time in the 802.3) which is greater than the RTD of 49 usec.
Hence the minimum frame size for the IEEE 802.3 (Ethernet) is 64 bytes.

## Slide 277: 802.3 Framing
Jam Signal: When a collision is detected during a frame transmission, the transmission is not terminated immediately. A station noting a collision has occurred sends a 4 to 6 bytes long pattern composed of 16 1-0 bit combinations.
The purpose of this is to ensure that any other nodes which may currently be receiving a frame will receive the jam signal in place of the correct 32-bit MAC CRC,
this causes the other receivers to discard the frame due to a CRC error.

## Slide 278: 802.3 MAC Address
An Ethernet MAC address consists of a 6-digit hexadecimal vendor OUI code followed by a 6-digit hexadecimal vendor-assigned value
OUI address is managed by IEEE. It has two bits that specify:
  Address is unicast or multicast
  Address is locally administered or globally unique

## Slide 279: 802.3 MAC
802.3 MAC uses CSMS/CD with binary exponential backoff
Binary Exponential Back off
  After collision wait 0 or more slots (of 51.2 msec)
  First collision: wait 0 or 1 slot (choose randomly)
  Second collision: wait 0, 1, 2 or 3 slots
  N-th collision: wait 0 - 2N -1 slots
  N max = 10 => wait between 0 - 1023 slots
  Give up after 16 trials and leave recovery to higher layers
Algorithm ensures low latency at low load and fairly resolves collisions when the load is high.

## Slide 280: 802.3 Performance Analysis
Assume constant transmission probability p (no exp back off)
Probability A of acquiring a slot (by one of k stations):
A  kp(1 p)k 1
Probability that contention interval, W, has precisely j slots:
A(1 A) j 1
Therefore, the average #slots per contention is given by
Each slot has a duration interval 2
Mean contention interval is W = 2/A
p optimal (= 1/k)  A = (1-1/k)k-1 =1/e (for k  heavy load) 
W=2e=5.4
A
jA(1 A) j 1  1


j 0

## Slide 281: 802.3 Standard
Channel Utilization
  Assume each frame takes T seconds to be transmitted.
  When many stations have frames to send
F=frame length,
L =cable length,
B=network rate,
c= propagation speed,
e=contention slots per frame
(Note: =L/c and T=F/B)
T 1
U 

T  2τ / A 1 2BLe/ cF

## Slide 282: Ethernet Switch
(b)
   
High-Speed Backplane or Interconnection fabric
(a)
Single collision domain
     

## Slide 283: Basic Ethernet Switch Architecture
Packet Classification Packet Scheduling Packet Switching
PHY
Transceiver
MAC
Egress Queue
Ingress Queue
PHY
Transceiver
MAC
Egress Queue
Ingress Queue
PHY
Transceiver
MAC
Egress Queue
Ingress Queue
PHY
Transceiver
MAC
Egress Queue
Ingress Queue
PHY
Transceiver
MAC
Egress Queue
Ingress Queue
PHY
Transceiver
MAC
Egress Queue
Ingress Queue
Control Processor

## Slide 284: Ethernet Switch
To improve the performance of the system, an Ethernet switch can be used
Each port of the system receives the frame of only one sender and stores it in the switch ingress buffers.
Central switch fabric reads the frames from ingress buffers and forwards it to the egress output buffers.
There will be no media collision
Depending on the traffic pattern, buffers can be filled which may results packet drop.

## Slide 285: Fast Ethernet
Media Transmission Speed: 100 Mbps
No multi-drop cables
Two modes of operation
  HUB Mode: a hub is a single collision domain. CSMA/CD is used
  Switched Mode: frames are buffered and switched in the hub/switch. No CSMA/CD. (100BaseFx works only in this mode)

## Slide 286: Fast Ethernet
Types of Media
  Twisted Pair: Most Common
    100 BaseTX: Operates in full duplex mode. Uses two UTP5 wires, one for transmission and one for reception. 4B/5B encoding at 125 MHz clock to send 100 Mbps.
  Fiber Optics
    100BaseFX: Operates in full duplex mode. Uses two strands of multimode fibers to transmit and receive 100 Mbps in each directions up to 2km.
    100BASE-SX: 100 Mbit/s Ethernet over multi-mode fiber. Maximum length is 300 meters.
    100BASE-BX10: 100 Mbit/s Ethernet bidirectionally over a single
strand of single-mode optical fiber.
    100BASE-LX10: 100 Mbit/s Ethernet up to 10 km over a pair of
single-mode fibers, using 1310 wavelength, full-duplex only.

## Slide 287: Gigabit Ethernet
Media Transmission Speed: 1 Gbps
Only Full duplex mode: send and receive independently to a switch and no media contention
Physical interfaces
  1000 base-X:
    Various standards for optical fiber-based transmission
    Supports multimode and single mode fibers
    Distance up to 120km
  1000base-T:
    Various standards for copper-based media
    Distance up to 100m

## Slide 288: 10 Gigabit Ethernet
Media Transmission Speed: 10 Gbps
Physical interfaces
  Copper based backplane:
    Used in backplane for high-speed communication between cards
    Distance up 1m
  Copper based cables:
    Coaxial cable, Twin-axial cables and twisted pairs
    Distance up to 100m
  Fiber-optic based cables:
    Multi-mode and single-mode fibers
    Distance up to 80km

## Slide 289: 25 Gigabit Ethernet
Media Transmission Speed: 25 Gbps
Physical interfaces
  Copper based backplane:
    Used in backplane for high-speed communication between cards
    Distance up 1m
  Copper based cables:
    Twin-axial cables up to 8m
    Twisted pair cable up to 30m
  Fiber-optic based cables:
    Multi-mode fiber up to 100m
    Single-mode fiber up to 30km using CWDM

## Slide 290: 40 Gigabit Ethernet
Media Transmission Speed: 40 Gbps
Physical interfaces
  Copper based backplane:
    Used in backplane for high-speed communication between cards
    Distance up 1m
  Copper based cables:
    Twin-axial cables up to 7m
    Twisted pair cable up to 30m
  Fiber-optic based cables:
    Multi-mode fiber up to 150m
    Single-mode fiber up to 40km

## Slide 291: 100 Gigabit Ethernet
Media Transmission Speed: 100 Gbps
Physical interfaces
  Copper based backplane:
    Used in backplane for high-speed communication between cards
    Distance up 1m
  Copper based cables:
    Twin-axial cable
    Distance up to 7m
  Fiber-optic based cables:
    Distance of 125m over multi-mode fiber
    Distance of 80km over single mode fiber

## Slide 292: Terabit Ethernet
Terabit Ethernet or TbE is Ethernet with speeds above 100 Gigabit Ethernet.
Media Transmission Speed: 200 Gbps and 400 Gbps
Physical interfaces
  Copper based backplane
  Copper based cables: Twin-Axial
  Fiber-optic based cables: Single Mode and Multi-Mode
  Chip to Chip Communication
Standards under development
  800 Gbps
  1.6 Tbps

## Slide 293: Ethernet Standard Trend

## Slide 294: Ethernet Speed and Reach

## Slide 296: Logical Link Control: 802.2
For some applications, an error-controlled, flow controlled connection is desired
Data link layer for 802
protocols consists of two parts:
  LLC logical link control
  MAC multiple access control
LLC implements the functionality as discussed in the data link layer section like:
  Error control
  Flow control
LLC offers three services:
  Unreliable datagram service
  Acknowledged datagram
service
  Reliable connection-oriented service
LLC header is based on the
HDLC protocol

## Slide 297: Global Wireless Standards
IEEE 802.15
Bluetooth
WAN
MAN
LAN
PAN
ETSI
HiperPAN
IEEE 802.11
WirelessLAN
ETSI
HiperLAN
IEEE 802.16
WirelessMAN
ETSI HiperMAN & HIPERACCESS
IEEE 802.20
(proposed)
3GPP, EDGE (GSM)

## Slide 298: Wireless Platforms
Fixed
Licensed and Unlicensed
E1/ T1 & DSL level service
Portable
Mobile
Licensed and Unlicensed Licensed
Consumer DSL level service Wideband Data Rates
802.16
HiperMAN
Enterprise
/ Backhaul
802.16
HiperMAN
Residential access
Nomadic
Cellular Wideband
2.5G, 3G
Destination based
802.11 Hot
Spots
802.16e

## Slide 299: Wireless LAN Protocols
Wireless protocols are inherently multiple access !
Can we use sensing ?
  What matters is collision at Rx
Hidden station problem:
  C can not sense A. If both target B, there will be a collision
Exposed station problem:
  B sends to A. C senses the medium and concludes that there is activity. So, it does not send to D. The link between C and D is not susceptible to the conversation of A and B.

## Slide 300: Wireless LAN Protocols
MACA: Multiple Access with Collision Avoidance
  Sender: sends RTS (request to send)
  Receiver: sends CTS (clear to send)
  RTS and CTS contain length of message to be sent

## Slide 301: Wireless LAN Protocols
Key observations:
  Any station hearing RTS must keep silent during the next phase of data transmission
  Any station hearing CTS must keep silent during next message

## Slide 302: Wireless LANs
Wireless LANs are becoming increasingly popular due to:
  Ease of installation
  Support of mobility
  Easy connection to back-bone networks in places like airports, shopping
centers, conference rooms, etc

## Slide 303: Wireless LAN
Key Architectures
  Infrastructure Mode: Require Access Point/Base Station
  Ad-Hoc Mode: On demand networking without infrastructure

## Slide 304: Wireless LANs
Several standards have been developed in the last decade
One of the hottest areas of telecommunication
The list of standards keeps growing every year!

## Slide 305: IEEE 802.11 Overview

## Slide 306: IEEE 802.11 PHY Review
802.11a Orthogonal Frequency Division Multiplexing (OFDM)
  Variable bit rates up to 54 Mbps
  Uses 5 GHz ISM band
  Much more immune to channel variations
  Short range, mostly used for indoor LANs
802.11b High Rate Direct Sequence
Spread Spectrum (HR-DSSS)
  Variable bit rate up to 11 Mbps (1,2,5.5,11)
  Uses 2.4 GHz ISM band
  Longer range than 802.11a (Can be used for inter-office LAN connection)
802.11n
802.11g (OFDM)
  Variable bit rate up to 54 Mbps
  Uses 2.4 GHz band
  OFDM/DSSS Modulation
  Up to 540 Mbps
  Uses 2.4 and 5 GHz bands
802.11ac (5 GHz)
  Uses MIMO and OFDM
  Up to 860 Mbps per stream
  Up to 8 MIMO streams

## Slide 307: Basics of OFDMA

## Slide 308: OFDMA in 802.11

## Slide 309: OFDMA in 802.11

## Slide 310: Overview of 802.11 MAC
All 802.11 (a,b,g) networks use the same MAC
MAC supports two modes of operation
  Distributed Coordination Function: Used for Ad-Hoc connections
  Point Coordination Function: Used when nodes are connected to an access point

## Slide 311: Overview of 802.11 MAC
PCF Mode:
  Base station broadcasts a beacon frame that contains frequency hopping, synch and some other information periodically
  Stations can sign up to the base for receiving services
  Once base station registers a user, it will assign the necessary resources.
  Base station can manage the activity of users by putting them in sleep mode to save battery power. It wakes them up when needed.

## Slide 312: Overview of 802.11 MAC
DCF employs CSMA/Ca that has two access methods
  Start transmitting as soon as channel is idle. If a collision, wait a random time (exponential back off) and try again
  Use MACAW using RTC/CTS
  Note: RTS and CTS contain data length thereby setting the waiting time (Not
Available Vector) in other stations.

## Slide 313: Overview of 802.11 MAC
A long frame has a much higher chance of error than a short frame
For BER=1e-4, Probability of frame error is more than 70% for a frame of length 12kbit.
Once channel is acquired, a burst of short frames can also be sent to increase system throughput
Uses Stop and Wait for each fragment

## Slide 314: Overview of 802.11 MAC
All stations should remain quiet for a certain period after a transmission has been completed (Inter Frame Space (IFS)) .
  Short Interframe Spacing (SIFS):
    High priority frames (ACK, CTS or fragment burst) only wait for SIFS duration
  Arbitration Interframe Space (AIFS)
    Base station can send high priority traffic during AIFS1 and low priority traffic during AIFS4
  DCF Interframe spacing (DIFS)
    Any station may attempt to acquire the channel to send a new frame after the medium has been idle for DIFS
  Extended Interframe spacing (EIFS)
    A station can report a bad or unknown frame during this time

## Slide 315: Overview of 802.11 MAC

## Slide 316: Overview of 802.11 MAC
Data
SIFS
Defer access
Ack
DIFS
NAV (RTS)
Source
Destination
Other
RTS
DIFS
SIFS
CTS
SIFS
NAV (CTS)
NAV (Data)

## Slide 317: Overview of 802.11 MAC
A station can send if channel is idle for a period of DIFS or longer
If medium is busy, node starts a random backoff timer
Station is allowed to transmit when its backoff timer expires during a
contention period
If another station starts transmission during the contention period, the backoff timer is suspended and resumed next time a contention period takes place
When a station has successfully completed a frame transmission and has another frame to send, the station must first execute the backoff procedure
Waiting stations tend to have smaller remaining backoff time and can access channel sooner. Therefore, a degree of fairness is provided in the channel access process.

## Slide 318: IEEE 802.11 services
A wireless LAN can provide these services:
  Distribution Services
    Association: A mobile can connect to base station using this service.
    Disassociation: Breaking the relationship between the base and mobile
    Re-association: Change the preferred base station by moving from one cell to another cell
    Distribution: A Service that determines how to route frames sent to a base
    Integration: A service that handles the required translation of frame format for
sending a packet to a non-802.11 format
  Station services
    Authentication: prove the identity of the mobile
    De-authentication: cancel the approved identification of a user
    Privacy: Encryption of messages sent over PHY
    Data Delivery: Transmission of data from one node to another

## Slide 319: Bluetooth (IEEE 802.15)
A standard for Inexpensive, compact , short range wireless communication.
Started by Ericsson, IBM, Nokia, Intel and Toshiba in 1994, Version
1.0 finalized in 1999.
Based on pico-nets connected together by slave bridges
Each piconet has one master node and seven slaves and up to 255 parked nodes (nodes in power stand-by)
Each piconet is a centralized TDM system managed by Master. All communications between slaves are done through the master. (No direct slave to slave comm.)

## Slide 320: Bluetooth Applications
Standard specifies the entire protocol stack for various applications.
Important defined profiles (Important applications which are standardized by the standard):
  Serial port emulator
  LAN Access
  Dial up networking
  Cordless telephony
  Intercomm
  Headset

## Slide 321: Bluetooth Evolution

## Slide 322: Bluetooth Protocol Stack
Physical Radio:
  Operates in 2.4 GHz ISM frequency band
Baseband Layer (MAC)
  Turns raw bits to frames and
defines key formats
  Each frame is transmitted over a “Link”.
  Two types of links:
    Asynchronous Connectionless (ACL) used for packet data
    Synchronous Connection Oriented (SCO) used for real time data such as voice
L2CAP:
Frame segmentation and re- assembly
Mux/Demux of multiple data
sources
Handles QoS requirements during link establishment and normal operation

## Slide 323: Ethernet Switching
How to know where to forward frames in an Ethernet Switch?
Forwarding Table

## Slide 324: MAC Address Table
Switches use MAC address tables to determine how to forward traffic between ports.
  MAC tables include dynamic and static addresses.
  The MAC address table was also referred to as content addressable memory (CAM) table.
  The maximum size of the MAC address table varies with different switches.
    For example, the Catalyst 2960 series switch can store up to 8,192 MAC addresses

## Slide 325: MAC Address Table
Static MAC addresses:
  A network administrator can specifically assign static MAC addresses to certain ports.
  Static addresses are not aged out.
  Only those devices that are known to the network administrator can connect to the network.

## Slide 326: Dynamic MAC Addresses
Backward Learning is used to dynamically update the MAC address table:
  If the port for the destination address is the same as the source port, discard the frame.
  If the port for the destination address and the source port are different, forward the frame on to the destination port.
  If the destination port is unknown, use flooding and send the frame on all ports except the
source port.
  Remove very old entries (to trace systems going down and other topology changes)

## Slide 327: Switching Hierarchy
Ethernet switches can be connected to expand the network
Backward learning is used to learn addresses in all switches

## Slide 328: Backward Learning Loop

## Slide 329: Spanning Tree Protocol

## Slide 330: Bridging
Bridges need to route packets at layer 2 and also do some frame conversions

## Slide 331: Virtual LAN (VLAN)
It is desirable to group users on LANs based on policy (For example based on organizational structure) rather than the physical layout of the building
  Security and access control
  Network Load Control
  Broadcast Traffic (ARP)
  Limiting scope of unwanted events such as broadcast storms

## Slide 332: Virtual LAN (VLAN)
Network partitioning in Layer 2 can be done by proper management of switch learning process.

## Slide 333: VLAN
Partition a switch into different switches
Use tags to identify VLANs
Communication Networkss
91
Pictures: https://www.thomas-krenn.com/en/wiki/VLAN_Basics

## Slide 334: IEEE 802.1Q
Tag protocol identifier (TPID): a 16-bit field set to a value of 0x8100 in order to identify the frame as an IEEE 802.1Q-tagged frame. This field is located at the same position as the EtherType/length field in untagged frames, and is thus used to distinguish the frame from untagged frames.

## Slide 335: IEEE 802.1Q
Tag control information (TCI)
  Priority code point (PCP): a 3-bit field which refers to the IEEE 802.1p class of service and maps to the frame priority level.
  Values in order of priority are: 1 (background), 0 (best effort), 2 (excellent effort), 3 (critical application), ..., 7 (network control).
  These values can be used to prioritize different classes of traffic (voice, video, data, etc.).
  Drop eligible indicator (DEI): a 1-bit field. (formerly CFI) May be used separately or in conjunction with PCP to indicate frames eligible to be dropped in the presence of congestion.

## Slide 336: IEEE 802.1Q
Tag control information (TCI)
  VLAN identifier (VID): a 12-bit field specifying the VLAN to which the frame belongs.
  The hexadecimal values of 0x000 and 0xFFF are reserved.
  All other values may be used as VLAN identifiers, allowing up to 4,094 VLANs.
  The reserved value 0x000 indicates that the frame does not belong to any VLAN; in this case, the 802.1Q tag specifies only a priority and is referred to as a priority tag

## Slide 337: IEEE 802.1Q
The VLAN fields are only actually used by the bridges and switches and not by the user machines.
There can be computers (and switches) that are not VLAN aware.
The first VLAN-aware bridge to touch a frame adds VLAN fields and
the last one down the road removes them.
Frames can be tagged depending on the port on which they are received.

## Slide 338: Data Communication Networks Network Layer
Communication Networkss
1
DR.Eslami
Department of Electrical Engineering
Islamic Azad University،Science And Research Branch

## Slide 339: The Network Layer
1 2 3 2 1
2 1
1 2 3
2
1
Medium
A
B
2 1
1 2 3
C
4 3 2 1
1 2 3 4
End system

End system

Network
1
2
Physical layer entity
Data link layer entity
3 Network layer entity
3
Network layer entity
Transport layer entity
4
Role of network layer: routing packets
  Deals with end-to-end communication
  Aware of network topology
  Choose appropriate route
  Communicates with transport and data
link layers
Network layer topics
  Design issues
  Routing algorithms
  Congestion control
  Quality of Service
  Internetworking
  Network layer in the Internet: IP
Data Communication Networks
2

## Slide 340: Network Layer Design Issues
Services provided to the transport layer
  Independent of chosen subnet technology
  Shield transport layer from topology, type and number of subnets
  Uniform numbering plan, across LANs and WANs
3
Network layer
Data link layer
Physical layer
Network layer
Data link layer
Physical layer
End system

Network layer
Data link layer
Physical layer
Network layer
Data link layer
Physical layer
Transport layer
Transport layer
Messages
Messages
Segments
End system

Network
service
Network
service

## Slide 341: Network layer design issues
Connection-oriented or connectionless service?
  Where to put the complexity?
Internet community: connectionless
  Network will be unreliable anyway => handle this issue in higher layer (s)
  Only SEND packet and
RECEIVE packet needed
  Hosts are getting powerful; so why not put the complexity there
(in the transport layer)
=> easy to adapt
  Speed more
important than accuracy

## Slide 342: Network Layer Design Issues
Telephone companies: NL should be connection-oriented
  Set up connection first
  Each connection has unique ID
  Negotiate parameters (quality, cost)
  Communication in both directions
  Use of Acknowledge gives automatic flow control

## Slide 343: Virtual Circuits & Datagrams
Virtual circuits :
  Avoid routing every packet or cell independently
  All packets/cells follow same route (= session routing)
  Store # VC in routing tables (consuming some resources)
Datagrams
  Each packet contains destination and is independently routed
  Also usable for
connection-oriented service

## Slide 344: Routing
Message / packet / cell has to pass multiple hops
Routing algorithm : decide which outgoing link to use
Routing algorithm requirements
  Correctness
  Simplicity
  Robustness: cope with changing topology
  Stability: converge quickly
  Fairness: guarantee progression

## Slide 345: Routing algorithms
Non-adaptive (static) routing:
  Do not use measurements or estimates of current traffic and topology
  Static routing: calculate route off-line or use deterministic algorithm
Adaptive (dynamic) routing:
  Routing decision depends on network status
  Update state information regularly
  What type of network information do we base the decision on?
    Hop count
    Distance, estimated transit time
    Traffic rate
    Congestion metrics

## Slide 346: Routing Algorithms: Flooding
Static algorithm
Idea: forward incoming packet on all other outgoing lines

## Slide 347: Routing Algorithms: Flooding
Reducing the number of forwarded packets using sequence numbers

## Slide 348: Routing Algorithms: Flooding
Flooding Properties:
  Not practical in most applications
  Generates too much traffic
  Useful for:
    Extreme robustness (military purpose)
    Broadcast
    Reference algorithm
  It always finds the shortest delay path !!

## Slide 349: Routing
Optimality principle:
  If F is on optimal path of L  B then the whole path F  A  B is the best path between F and B
Consequence: optimal routes from all sources to a given root ( = sink node ) form a sink tree  no loops.

## Slide 350: Shortest Path Algorithm
Shortest Path Algorithm is used as part of many routing algorithms
Build router graph G(N, L)
  N is the set of nodes
  L is the set of links (or edges)
Choose path metric (weight of lines L)
  # hops
  Estimated delay ( using echo packets )
  Physical distance
  Queue length ( of outgoing lines )

## Slide 351: Shortest Path Algorithm
Dijkstra’s shortest path algorithm:
Steps to find all shortest paths from A
Initially: make A permanent: P = {A} : label all neighbors k of A with Dk =dAk
Repeat until P contains all nodes
  find next closest node and add it to P:
  P= P + {i} , with Di = min Dk (k not in P)
  Updating labels of neighbours of P
  Dk = min [ Dk , Dk + dik ] (k not in P)
Key fact: the path to the next closest node i has to go through nodes
from P only.

## Slide 352: Shortest Path Algorithm
 | Base Set | B | C | D | E | F | G | H
0 | A | 2,A |  |  |  |  | 6,A | 
1 | A,B |  | 9,B |  | 4,B |  | 6,A | 
2 | A,B,E |  | 9,B |  |  | 6,E | 5,E | 
3 | A,B,E,G |  | 9,B |  |  | 6,E |  | 9,G
4 | A,B,E,G,F |  | 9,B |  |  |  |  | 8,F
5 | A,B,E,G,F,H |  | 9,B | 10,H |  |  |  | 
6 | A,B,E,G,F,H,C |  |  | 10,H |  |  |  | 

## Slide 353: Shortest Path Algorithm
 | Base Set | B | C | D | E | F | G | H
0 | A | 2,A |  |  |  |  | 6,A | 
1 | A,B |  | 9,B |  | 4,B |  | 6,A | 
2 | A,B,E |  | 9,B |  |  | 6,E | 5,E | 
3 | A,B,E,G |  | 9,B |  |  | 6,E |  | 9,G
4 | A,B,E,G,F |  | 9,B |  |  |  |  | 8,F
5 | A,B,E,G,F,H |  | 9,B | 10,H |  |  |  | 
6 | A,B,E,G,F,H,C |  |  | 10,H |  |  |  | 

## Slide 354: Shortest Path Algorithm
 | Base Set | B | C | D | E | F | G | H
0 | A | 2,A |  |  |  |  | 6,A | 
1 | A,B |  | 9,B |  | 4,B |  | 6,A | 
2 | A,B,E |  | 9,B |  |  | 6,E | 5,E | 
3 | A,B,E,G |  | 9,B |  |  | 6,E |  | 9,G
4 | A,B,E,G,F |  | 9,B |  |  |  |  | 8,F
5 | A,B,E,G,F,H |  | 9,B | 10,H |  |  |  | 
6 | A,B,E,G,F,H,C |  |  | 10,H |  |  |  | 

## Slide 355: Shortest Path Algorithm
 | Base Set | B | C | D | E | F | G | H
0 | A | 2,A |  |  |  |  | 6,A | 
1 | A,B |  | 9,B |  | 4,B |  | 6,A | 
2 | A,B,E |  | 9,B |  |  | 6,E | 5,E | 
3 | A,B,E,G |  | 9,B |  |  | 6,E |  | 9,G
4 | A,B,E,G,F |  | 9,B |  |  |  |  | 8,F
5 | A,B,E,G,F,H |  | 9,B | 10,H |  |  |  | 
6 | A,B,E,G,F,H,C |  |  | 10,H |  |  |  | 

## Slide 356: Shortest Path Algorithm
 | Base Set | B | C | D | E | F | G | H
0 | A | 2,A |  |  |  |  | 6,A | 
1 | A,B |  | 9,B |  | 4,B |  | 6,A | 
2 | A,B,E |  | 9,B |  |  | 6,E | 5,E | 
3 | A,B,E,G |  | 9,B |  |  | 6,E |  | 9,G
4 | A,B,E,G,F |  | 9,B |  |  |  |  | 8,F
5 | A,B,E,G,F,H |  | 9,B | 10,H |  |  |  | 
6 | A,B,E,G,F,H,C |  |  | 10,H |  |  |  | 

## Slide 357: Shortest Path Algorithm
 | Base Set | B | C | D | E | F | G | H
0 | A | 2,A |  |  |  |  | 6,A | 
1 | A,B |  | 9,B |  | 4,B |  | 6,A | 
2 | A,B,E |  | 9,B |  |  | 6,E | 5,E | 
3 | A,B,E,G |  | 9,B |  |  | 6,E |  | 9,G
4 | A,B,E,G,F |  | 9,B |  |  |  |  | 8,F
5 | A,B,E,G,F,H |  | 9,B | 10,H |  |  |  | 
6 | A,B,E,G,F,H,C |  |  | 10,H |  |  |  | 

## Slide 358: Shortest Path Algorithm
 | Base Set | B | C | D | E | F | G | H
0 | A | 2,A |  |  |  |  | 6,A | 
1 | A,B |  | 9,B |  | 4,B |  | 6,A | 
2 | A,B,E |  | 9,B |  |  | 6,E | 5,E | 
3 | A,B,E,G |  | 9,B |  |  | 6,E |  | 9,G
4 | A,B,E,G,F |  | 9,B |  |  |  |  | 8,F
5 | A,B,E,G,F,H |  | 9,B | 10,H |  |  |  | 
6 | A,B,E,G,F,H,C |  |  | 10,H |  |  |  | 

## Slide 359: Shortest Path Algorithm
 | Base Set | B | C | D | E | F | G | H
0 | A | 2,A |  |  |  |  | 6,A | 
1 | A,B |  | 9,B |  | 4,B |  | 6,A | 
2 | A,B,E |  | 9,B |  |  | 6,E | 5,E | 
3 | A,B,E,G |  | 9,B |  |  | 6,E |  | 9,G
4 | A,B,E,G,F |  | 9,B |  |  |  |  | 8,F
5 | A,B,E,G,F,H |  | 9,B | 10,H |  |  |  | 
6 | A,B,E,G,F,H,C |  |  | 10,H |  |  |  | 
7 | A,B,E,G,F,H,C,D |  |  |  |  |  |  | 

## Slide 360: Dynamic routing
Distance vector routing
  Used in early ARPANET
  Each router maintains distance table indexed by destination number
  Entry contains : outgoing link + estimated distance
How to know distance?
  Send echo packet to all neighbors; this packet gets back with timestamp
therefore, distance to neighbor is determined
Receive regularly updated tables from neighbors and update own table
  D (a,b) = min (D (a,x) + D (x,b) )
{for all neighbors x}
Other metrics such as hop count
or cost could also be used

## Slide 361: Dynamic routing

## Slide 362: Distance vector routing
Count-to-infinity problem:
  Good news propagates much faster than bad news
Split Horizon hack: (one of many efforts to reduce the impacts of this problem)
  C does not report B the distance of node X for which packets have to flow through B
  C tells D the truth about the distance to A, but tells B that CA= 
  When AB fails, the bad news propagates as quickly as the good news
Failure of Split Horizon
  Init: CD=1, AD=2, BD=2, AB=1
  CD fails, A and B tell C they can’t reach D, so C sets CD=
  Unfortunately, A hears from B that BD=2, so it sets AD=3 => wrong!

## Slide 363: Link State Routing
Solves slow convergence problem of the distance vector approach
Idea:
  Send all nearest neighbor information to all other routers
  Each router uses this information to know the topology and determines shortest path to all nodes
Link State Routing: 4 steps
  Discover neighbors (and their IDs)
  Measure delay (or cost) to reach neighbours
  Send link state packets to all other routers
  Compute topology and shortest path to every router
Perform last three steps at
  Regular intervals
  When major event happens (link / node going down or coming up )

## Slide 364: Link State Routing
Discover neighbor:
  After booting, send HELLO packet to all neighbors
  Neighbor should respond telling its identity
Measure delay:
  Send ECHO packet; neighbors respond immediately
  Calculate trip time = delay/2
  Average of multiple measurements may be used

## Slide 365: Link State Routing
Sending link state packets:
  Make link state packet
  Use flooding to distribute packets to all routers
  Use sequence numbers to reduce traffic
  Routers keep (source, seq#) pairs and discard lower sequence numbers
  Use age fields to handle corrupted sequence numbers
  Age is decremented in regular intervals
  Information is discarded when age is zero

## Slide 366: Link State Routing

## Slide 367: Link State Routing
Route Calculation
  Compute new routes (when packets from all sources have been received):
  use shortest path algorithm on each node (e.g., Dijkstra’s algorithm)
Link state routing used widely.
  Example: OSPF (open shortest path first) routing which is used in the Internet
Problem with Link State Routing:
  large memory requirements ~ O (NK), where: N=number of routers K=network node degree

## Slide 368: Hierarchical Routing
Data Communication Networks
Purpose: Reduce routing table size and routing computation time
Solution: use multi-level topology

## Slide 369: Broadcast Routing Methods
Send lots of individual packets
  Lots of traffic
  Source needs to know all destination addresses
  Generally, not used
Flooding
  Generates too many packets
Multi-destination routing
  Packet contains list of destinations
  Router splits packet among output lines and updates destination
list
  Again, all destination addresses must be known!

## Slide 370: Broadcast Routing Methods
Sink tree (= spanning tree)
  Each packet is sent along the lines of the sink tree of the sender
  Most efficient method for broadcast to all
  Sink tree is not always known (e.g., not when distance vector routing is used; link state routing does have this knowledge!)

## Slide 371: Broadcast Routing: Reverse Path Forwarding
Reverse path forwarding
  Does not require network knowledge
  Easy to implement
  Transmission automatically finishes
  Reasonably efficient
  No list of destinations needed
  No special mechanism needed to stop the forwarding
Each router knows the normal line for sending packets to all other routers
When a packet is received from a router, it is checked to see if it is coming from the “normal” line.
Send packet to all neighbours, but discard incoming packets from ‘wrong’ lines
Packets from A arriving at B on line L is ‘wrong’ if B does not send to A at line L
The idea is that if a packet arrives at the wrong line, it probably did not follow the shortest route
The overall total generated traffic is slightly more than required, but efficiency is
reasonable

## Slide 372: Broadcast Routing: Reverse Path Forwarding

## Slide 373: Multicast Routing
Multicast: Sending packets to a group of nodes => Group management required
Routers must know to which groups their hosts belong
Each router computes spanning tree for each supported group
Multicast packets are then forwarded to appropriate spanning trees
only
When multiple spanning trees share some paths, trees need to be pruned to limit the packet forwarding only to the relevant routers

## Slide 374: Ad-Hoc Routing
Ad Hoc Networks: Network of nodes that just happens to be near each other. Nodes can move and start/stop working arbitrarily. Examples:
  Military vehicles on battlefield. (No infrastructure.)
  A fleet of ships at sea. (All moving all the time)
  A gathering of people with notebook computers.
Fixed-wire Routing techniques can’t be used anymore
Several methods have been proposed for ad hoc routing. Examples are:
  Dynamic Source Routing (DSR)
  Ad hoc On-demand Distance Vector (AODV) Routing
Key issue for Ad Hoc routing methods is that routes are calculated on-demand to save bandwidth and battery life

## Slide 375: Dynamic Source Routing (DSR)
On Demand routing protocol designed to restrict the routing overhead in ad hoc networks
Route Request (RRQ) packets are generated by source and flooded in the network to inquire about a possible route to destination
Each Route Request carries a sequence number generated by the source node and the path it has traversed.

## Slide 376: Dynamic Source Routing (DSR)
Each node, upon receiving a RRQ
packet:
  Checks the sequence number, records it and checks it to avoid forwarding duplicates
  Checks time to live (TTL) of the packet to avoid forwarding old packets.
  Adds its own ID to the packet
  Rebroadcasts the packet to its neighbors
Destination node replies to the source node using the trace ID of the first arrived RRQ packet.
Source sends its data packets with a header containing the entire routing path. (That is why it is called source routing)

## Slide 377: Ad-hoc On-demand Distance Vector (AODV) Routing
Node A constructs a ROUTE REQUEST (RRQ) packet and broadcasts it.
RRQ Contains:
  Request ID: a local counter maintained separately by each node, incremented for each RRQ packet it sends
  {Source Address, Request ID} uniquely identify the RRQ packet
  Destination Sequence Number (Dest_Seq#): Number identifying the last known value of Route Reply (RRP) from the desired destination
Each node that hears the RRQ discards it if it is a duplicate
Then it looks in the route table. If there is a fresh route to the destination, it sends a RRP to the source with the info (Saying: Send the packet to me and I’ll route it!)
Fresh route: Dest_Seq# of the RRQ is larger than the Dest_Seq# that exist in its routing table
If it does not know the route, it increments the Hop count and re-broadcasts it.
It also extracts the source data and uses it for reverse routing (Everybody
knows where is A)

## Slide 378: AODV
The message goes up to the destination (In this example, node I)
I builds an RRP, where the Hop count, source and destination address are copied from RRQ,
Dest_Seq# is copied from its current local counter value
Life Time: Controls how long the route is valid
Packet is sent back to the source address.
In the reverse path, every node knows how to get back to the source.

## Slide 379: AODV Route Maintenance
Routing info should be updated regularly because of node’s changing status
Periodically, each node sends a Hello message to its neighbors
If no response to Hello or no response to a data packet, assume the neighbor is dead
Active neighbors of node D: The neighbors that depend on D for routing their packets.
When a neighbor goes down, the affected active neighbors are informed of the event. Local routing table is modified to delete the route passing through the dead node.
Each of those nodes in turn would notify their affected active neighbors of the event.
The routing tables are modified all over the nodes and invalid routes are
purged.

## Slide 380: Congestion control
Problem: Network performance severely degrades at high load
Examples of Reasons:
  N to 1 communication: Hot-spot
  Sudden burst of traffic

## Slide 381: Congestion Control
What is the difference between congestion control and flow control
  Congestion control
    Global issue (network)
    Indirect feedback
    Sometimes slowdown messages are used
  Flow control
    Local issue (line, point-to-point connection )
    Direct feedback from neighbor

## Slide 382: Congestion Control
Time Scale of applying congestion control techniques

## Slide 383: Principles of Congestion Control
Systems can be controlled by an open loop or a closed loop mechanism
Open loop: no feedback; solve problems at design time (to make sure they
never occur; worst case design)
Open loop issues:
  No regard to current state of network
  When to accept or discard new traffic? (Admission Control)
Closed loop: Monitor the network on congestion
  Metrics: % discarded packets, queue length, # timed out packets, average delay
Pass this information to right place
  Feedback packets: increase load
  Reserved bit field in header of every packet
  Probe packets can be sent periodically (ask about congestion)
Adjust system operation
  Avoid oscillation (proper response time needed)
  Increase number of resources
  Decrease load

## Slide 384: Congestion Prevention
Open loop policies can be applied at different layers
Data link layer policies
  Retransmission creates extra packets
    Tune time out time
Use selective repeat instead of go back n
Acknowledgement policy
  Use piggyback
Tight flow control (small window)
Network layer policies:
  Any congestion control policies work only with virtual circuits, e.g.. reserving space
  Routing
    Spread traffic
    Avoid hot spots
  Discard policies
    Remove long life-time packets
Transport layer policies:
Similar as previous policies
Choose proper time-out value for sender

## Slide 385: Congestion Control
Congestion Control in Virtual Circuit subnets:
  Use Admission Control to prevent congestion
    If there is congestion, don’t accept new traffic.
    Reserve the necessary resource along the data path to
prevent congestion
  Negotiate a new VC that does not pass through the congested area

## Slide 386: Congestion Control in Datagram subnets
Estimate congestion u by sampling certain activity f
(e.g. Line utilization) on each outgoing line
 (1 a) f
Calculate u using:
unew  auold
Warning bit
  Set a bit in the ip payload indicating that there is congestion along the data path. (Give warning when u > threshold)
  The transport entity copies this bit in the acknowledge and send it back to the source
  The source can estimate the congestion by measuring the fraction of ACKs it receive with a congestion bit indication

## Slide 387: Congestion Control in Datagram subnets
Data Communication Networ
ks 50
Choke packets
  Don’t wait for the destination to act. It may
be too late!
  Each router sends a choke packet to source when in warning state.
  Source reduces the load by %X. waits for a period of time and if there was no more choke packets, goes back to normal operation
Hop-by-hop choke packets
  Choke packets may take a long time to cause effect
  Solution: Choke packets should not effect the source host only, but also intermediate routers
  Routers reduce traffic in certain direction
  More buffer space required at routers !!

## Slide 388: Buffer Management
Load Shedding
  Allow routers to discard packets
  What‘s the selection criterion ?
  Use packet priority
    Use priority field to decide which packet to drop
    Users should pay more for higher priority packets

## Slide 389: Buffer Management
It is best to drop packets as soon as there is congestion
If there is congestion in a particular port, it is difficult to know whose fault it is (Or who is the source that has caused the congestion)
Don’t send choke packets as it can add to the congestion
TCP would slow down if packets are dropped (Reduced traffic rate from the source). This is implicit feedback from the network about its status.

## Slide 390: Random Early Detection (RED)
This is a proactive buffer management approach in which the router discards one or more packets before the buffer becomes completely full
Average Queue Length (avg): Moving average of the Queue length in the past
𝑎𝑣𝑔 𝑡 + 1 = 𝑎𝑣𝑔 𝑡 × 1 − 𝛼 + 𝐿(𝑡) × 𝛼
Packets are marked with a probability P as a function of avg
The probability that a packet is marked from a particular connection is roughly proportional to that connection’s share of the bandwidth at the router.
The minimum and maximum thresholds minth and maxth are determined by the desired average queue size.
The average queue size that makes the desired tradeoffs such as the tradeoff between maximizing throughput and minimizing delay depends on network characteristics
Advanced Communication Networkss (Sharif U of Tech)

## Slide 391: Random Early Detection (RED)
Advanced Communication Networkss (Sharif U of Tech)

## Slide 392: Traffic Shaping
Traffic shaping is used to avoid bursty traffic
  Regulate the average rate on server side
  Negotiate a contract between sender and network. (Service Level Agreement (SLA))
  Specially important for real-time applications
Traffic control
  Leaky bucket
  Token bucket
  Hybrid solution

## Slide 393: Traffic Shaping – Leaky Bucket
Leaky bucket algorithm
  Sender puts packets or bytes in a queue
  When queue is full the input is discarded
  Queue output data at constant packet or byte rate
  Equal to a single-server queuing system with constant service time

## Slide 394: Traffic Shaping -Token Bucket
Token bucket algorithm
  Bucket holds tokens, generated 1 per T sec. up till certain max. value
  Idle host time builds up ‘transmission rights’ (= tokens)

## Slide 395: Traffic Control Example
(a) Input to a leaky
bucket.
(b) Output from a leaky bucket.
Output from a token
bucket with capacities of
  (c) 250 KB,
  (d) 500 KB,
  (e) 750 KB,
  (f) Output from a 500KB token bucket feeding a 10-MB/sec leaky bucket.

## Slide 396: Resource Reservation
Resource Reservation
  To provide QoS, some sort of fixed path for the flow seems to be necessary
  The idea: Reserve critical resources along the path of a flow
  Critical Resources:
    Bandwidth
    Buffer space
    CPU processing cycle (This can be tricky)
Example for resource relation:
  Mean processing capacity of the
processor, =106 packets/sec
  Mean arrival rate of packets to the processor (Poisson distribution),
=0.95 106 packets/sec
  Mean delay experienced by a packet is:
So, the port bandwidth, buffer space requirement and processing capacity all are related and impact QoS parameters.
 20 sec
1 0.95
1
T  1 sec
1 1

    T    1 

## Slide 397: Admission Control
The flow can be specified in multiple ways.
Sender generates the flow spec and sends it to the destination
Routers along a flow-path will study the flow parameters, reserve enough resources and reduce the requested level of service if they can’t meet it.
At the other end, a decision will be made on the provided QoS to the flow (control the flow admission by reservation of resources)
An example of flow specification (RFC2210):
  Token Bucket Rate (Bytes/sec) (Maximum sustained transmitter rate)
  Token bucket size (Bytes) (Maximum burst size)
  Peak data rate (Bytes/sec)
  Minimum packet size (Bytes)
    CPU cycles are used for each processed packet regardless of its size. This will help the router in its CPU allocation decision
  Maximum packet size (Bytes)
    Used for buffer allocation decision

## Slide 398: Explicit Congestion Notification
If there is a congested router, it marks the IP packets.
Receiver sends a congestion notification on the reverse path to notify the sender so it can reduce its traffic rate temporarily.

## Slide 399: Fair Queuing
If multiple sources compete for the same destination port of a router, then
the most aggressive sender can block all others
To remedy that, Fair Queuing algorithm was proposed:
  Go round robin around among senders, send one packet of each source on the destination port.
What if packet sizes are different?
  Go round robin, byte by byte on packets. When a packet got all its credits, send it
out

## Slide 400: Weighted Fair Queuing
We can assign weight to queues and consider the length of packets to allow fair service.
Priority of service is determined by calculating the virtual finish time of each packet.

## Slide 401: Jitter Control
For audio/video streaming applications, variance of delay (Jitter) should be controlled
Buffering at the destination can be used to reduce the effects of network-induced
Jitter on the packet arrival time.

## Slide 402: Quality of Service (QoS)
QoS parameters:
  Reliability
  Rate/Throughput
  Delay/Jitter
Applications require different types of QoS

## Slide 403: Internetworking
How to connect and route on networks using different protocol stacks
  Different protocols will always exist (vendor policies)
  Cheaper networks encourage variety (it becomes a departmental decision)
Interconnection of different networks is called an internet

## Slide 404: Internetworking
Various boxes connecting networks or segments are used:
Physical layer: Repeaters
  Copy individual bits between cable segments
Data link layer: Bridges, L2 Switches
  Store and forward data link frames between LANs
Network layer: Multi-protocol routers
  Forward packets between dissimilar networks (often called gateways)
Transport layer: Gateways
  Connect byte streams in the transport layer e.g. TCP socket connection
Application gateways:
  Proxy servers
  Firewall

## Slide 405: Internetworking
How networks differ?
  Connectionless service may change the order of packets
  Protocol conversion: e.g.. From IP to IPX
  Address conversion (range, hierarchy)
  Quality of service may or may not be provided
  Different packet length
  Different methods
(if at all) for flow control, security, accounting, etc.

## Slide 406: Tunneling
Tunnelling
  If source and destination hosts are on same type of network but there is a different network in between, tunnelling can be used
  Packet encapsulation performed by multi protocol router

## Slide 407: Fragmentation
All networks impose maximum packet payload size (Example: 65,515 bytes in IP)
Multi protocol routers (gateways) may fragment packets. Two options:
  Transparent :
    Packet leaves network unfragmented and fragments have to use same route
  Non-transparent
    Fragments reassembled at destination host
    All hosts must support this assemble feature
    Added overhead for all packets
Problem: if one fragment lost, end-to-end retransmission required
Another approach: choose smallest unit which every network can handle
Always chop large packets to this size and follow the same procedure

## Slide 408: The Internet Network Layer: IP
Internet: The Internet is an interconnected collection of many networks
IP = Internet Protocol (provides datagram service)
Transport layer breaks messages up in datagrams of about 1500 bytes
Datagrams are reassembled at destination host (by Transport layer)

## Slide 409: The Internet Network Layer: IP
IP datagram contains a header of minimal 20 bytes, containing fields for:
  Version (= 4 for IPv4)
  IHL: internet header length
  Differentiated services
    Distinguish between different
classes of service.
Total length
Identification
  Label fragments belonging to same datagram
DF (do not fragment) bit
Note: datagrams < 576 bytes should be supported

## Slide 410: The Internet Network Layer: IP
MF (more fragments) bit: is this the final fragment?
Fragment offset: Location of the
fragment within the datagram
TTL (time to live)
  Counter decremented at each hop
  Discard datagram when zero: send
control message back to source
Protocol field:
  Indicate which transport layer protocol
to use: e.g.. UDP or TCP
  Allows direct delivery to right TL protocol handler
Header checksum
Source and Destination IP addresses

## Slide 411: The Internet Network Layer: IP
Every IP-host (on the net) needs unique 32-bit address
Assignment by ICANN (Internet Corporation for Assigned Names and Numbers)
Five classes: A - E
Dotted decimal notation: Example: 129.245.96.122

## Slide 412: Subnets
A single class A, B or C address refers to one network.
The network can be designed to contain subnets that can be used for
internal routing.

## Slide 413: Subnet routing: How is routing performed:
Normally router contains table with the following type of addresses
  (network#, 0)
  (this network#, host#)
  This is a 2-level hierarchy
  If incoming network address not listed send packet to default router (with more extensive table)
With subnetting (for internal use only):
  Router table contains additional entries:
    (this network#, subnet#, 0)
    (this network#, this subnet#, host#)
  3-level hierarchy
  Use host masking to quickly determine subnet
Decision on how many bits to use for subnet and how many bits for Host addresses is an internal design parameter for each company or university

## Slide 414: Classless Inter Domain Routing
Idea: assign the addresses on a variable-sized blocks, without regard to
classes
Use Masking to quickly determine outgoing link
Masking example:
  Assume company needs 2k addresses, and gets: 194.24.0.0 - 194.24.7.255 (8 C blocks)
  Mask = 255.255.248.0 (248 = 1111.1000b)
  CIDR Notation: 194.24.0.0/21
Routing tables contain (base address, mask) triples
Incoming address is masked with each entry
If: (address AND mask) = base address, send packet to appropriate output port

## Slide 415: Longest Prefix Matching
The router compares the destination IP address, bit-by-bit, with the entries in the routing table.
The entry that has the longest number of network bits that match the IP destination address is always the best match (or best path)
  Example: Packet has a destination address 192.168.1.33
  Which path to choose?
Address | Converted Binary Address
192.168.1.33 (destination IP address) | 11000000.10101000.00000001.00100001
192.168.1.32/28 | 11000000.10101000.00000001.00100000 (<–Best match)
192.168.1.0/24 | 11000000.10101000.00000001.00000000
192.168.0.0/16 | 11000000.10101000.00000000.00000000

## Slide 416: Network Address Translation
Allow each host in the internal network to maintain a permanent private IP address.
Replace the {TCP Source, IP source} addresses with {virtual TCP source, Virtual IP
source} of each outgoing IP packet
On the reply, use the combination of TCP and IP addresses to lookup the local host
Reserved NAT addresses
  IP packets with these addresses should not appear on internet
  10.0.0.0 – 10.255.255.255/8 (16,772,216 hosts)
  172.16.0.0 – 172.31.255.255/12 (1,0478,576 hosts)
  192.168.0.0 – 192.168.255.255/16 (65,636 hosts)

## Slide 417: Network Address Translation

## Slide 418: Network Planes
Network systems contain:
  Data Plane
  Control Plane
  Management Plane

## Slide 419: Internet Control Protocols
Example of Internet Control protocols:
  Internet Control Message Protocol (ICMP)
  Address Resolution Protocol (ARP)
  Dynamic Host Configuration Protocol (DHCP)

## Slide 420: ICMP
A protocol to exchange messages between routers to allow
proper operation of the network
Messages are embedded in IP packet

## Slide 421: Address Resolution Protocol (ARP)
The Address Resolution Protocol (ARP) is a communication protocol used for discovering the link layer address, such as a MAC address, associated with a given internet layer address, typically an IPv4 address
Example:
  System A broadcasts ARP Request message on LAN : give me the Ethernet address of 141.23.56.23
  All LAN nodes receive the message, only the target unicasts the reply.
Address mappings are cached temporarily

## Slide 422: Address Resolution Protocol (ARP)
Remote Address Example: Host 1 wants to send information to Host 4
  Host 1 uses ARP message; gateway responds
  Host 1 Sends packet directly to gateway. (Host 1 must know the default (gateway) Ethernet address)
  Routers forward the packet to the destination LAN
  On destination LAN ARP is used by the router again to get the destination
Ethernet address

## Slide 423: Dynamic Host Configuration Protocol (DHCP)
DHCP: Dynamic Host Configuration Protocol (RFC 2131, 2132)
  A client-server architecture for configuration of host IP addresses
  A newly booted workstation broadcasts a DHCP DISCOVER packet
  The DHCP server replies by giving it an IP address
  The IP address is leased for a period of time.
  Host must ask for renewal of the lease before it expires.
  If the lease expires, the IP is returned to the pool of available IP addresses.
  If DHCP server is not on the same LAN, a DHCP proxy can relay the DHCP messages over network to the DHCP server.
  DHCP proxy should know the IP address of the DHCP server.

## Slide 424: DHCP Example

## Slide 425: DHCP Example

## Slide 426: DHCP Example

## Slide 427: Routing: Control Plane and Data Plane

## Slide 428: Router Architecture

## Slide 429: Input Port Processing
Line Termination
Data Link Processing
Address Lookup
Queuing

## Slide 430: Switching

## Slide 431: Output Port Processing
Queuing (Buffer management)
Data Link Processing
Line Termination

## Slide 432: Routing on the Internet
Internet is made up of many independent networks or ASs (Autonomous
Systems) that are connected.

## Slide 433: Internet Routing Protocols
Intradomain Routing (Interior Gateway Protocol)
Routing protocols used inside an AS.
OSPF and IS-IS are popular protocols.
Interdomain Routing (Exterior Gateway Protocol)
Routing protocols between ASs.
BGP protocol is widely used.

## Slide 434: Open Shortest Path First (OSPF)
OSPF is a link-state protocol that uses flooding of link- state information and a Dijkstra’s least-cost path algorithm.
With OSPF, each router constructs a complete topological map (that is, a graph) of the entire autonomous system.
Each router then locally runs Dijkstra’s shortest-path algorithm to determine a shortest-path tree to all subnets, with itself as the root node.

## Slide 435: OSPF Features
Security.
  Exchanges between OSPF routers (for example, link-state updates) can be authenticated.
  With authentication, only trusted routers can participate in the OSPF protocol within an AS, thus preventing malicious intruders from injecting incorrect information into router tables.
Multiple same-cost paths.
  When multiple paths to a destination have the same cost, OSPF allows multiple paths to be used

## Slide 436: Open Shortest Path First (OSPF)

## Slide 437: Hierarchy in OSPF
An OSPF autonomous system can be configured hierarchically into areas.
Each area runs its own OSPF link-state routing algorithm, with each router in an area broadcasting its link state to all other routers in that area.
Within each area, one or more area border routers are responsible for routing packets outside the area. Lastly, exactly one OSPF area in the AS is configured to be the backbone area.
The primary role of the backbone area is to route traffic between the other areas in the AS.
The backbone always contains all area border routers in the AS and may contain non-border routers as well.
Inter-area routing within the AS requires that the packet be first routed to an area border router (intra-area routing), then routed through the backbone to the area border router that is in the destination area, and then routed to the final destination.

## Slide 438: Border Gateway Protocol (BGP)
A decentralized protocol that is used to connect all ASs that are connected to form the internet.
In BGP, packets are not routed to a specific destination address, but instead to CIDRized prefixes, with each prefix representing a subnet or a collection of subnets.
  Router forwarding table entry example: (138.16.68/22,K) where K is the interface number of the router.

## Slide 439: Border Gateway Protocol (BGP)
BGP main objectives:
  Obtain prefix reachability information from neighboring ASs.
    BGP allows each subnet to advertise its existence to the rest
of the Internet.
  Determine the “best” routes to the prefixes.
    The best route will be determined based on policy as well as the reachability information.

## Slide 440: Example: IP Routing in Subnet

## Slide 441: Example: IP Routing in Subnet

## Slide 442: Hierarchical Addressing and Route Aggregation

## Slide 443: Border Gateway Protocol (BGP)
In BGP pairs of routers exchange routing information over semi-permanent TCP connections
Each such TCP connection, along with all the BGP messages sent over the connection, is called a BGP connection.
Furthermore, a BGP connection that spans two ASs is called an external BGP (eBGP) connection
A BGP session between routers in the same AS is called an internal BGP (iBGP) connection.

## Slide 444: BGP Example 1

## Slide 445: BGP Example 1
Gateway router 3a sends an eBGP message “AS3 x” to
gateway router 2c.
Gateway router 2c then sends the iBGP message “AS3 x” to all the other routers in AS2, including to gateway router 2a.
Gateway router 2a then sends the eBGP message “AS2 AS3 x” to gateway router 1c.
Gateway router 1c uses iBGP to send the message “AS2 AS3 x” to all the routers in AS1.
  Now, all routers in AS1 know that the subnet x is reachable via the path AS2-AS3-x

## Slide 446: BGP Example 2

## Slide 447: BGP Example 2
When a router advertises a prefix across a BGP connection, it includes with the prefix several BGP attributes.
A prefix along with its attributes is called a route.
Two of the more important attributes are AS-PATH and NEXT-HOP.
The AS-PATH attribute contains the list of ASs through which the
eBGP advertisement has passed.
The NEXT-HOP is the IP address of the router interface that begins the AS-PATH.
In this example, each router in AS1 becomes aware of two BGP
routes to prefix x:
  IP address of leftmost interface for router 2a; AS2 AS3; x
  IP address of leftmost interface of router 3d; AS3; x

## Slide 448: BGP Route Selection
A router learns all routes to a given prefix and performs route selection based on:
  Local preference of the route which can be assigned based on the policy of the network operator
  Shortest AS path which is the lowest number of ASs in the
route
  Shortest path from each router to the next-hop

## Slide 449: BGP Policy
One of the most important aspects of BGP is that it is designed so that network owners can apply their policy in routing.
Examples of policy:
  Any traffic flowing across an ISP’s backbone network must have either a source or a destination (or both) in a network that is a customer of that ISP.
  Use AS1 instead of AS2 because it is cheaper.
  Don’t use AT&T in Australia because performance is poor.
  Traffic starting or ending at Apple should not transit Google

## Slide 450: IPv6 Protocol
To expand the feature set and capabilities of IP, in 1990 work on new protocol started with these requirements:
  Support billions of hosts
  Reduce routing table size
  Simplify protocol (reduces processing power requirement in routers)
  Better security (authentication and privacy)
  Multicasting
  Mobile hosts
  Allow protocol to evolve (room for expansion)
  Coexist with IPv4
Important Features:
  Longer addresses than IPv4: 16
byte addresses
  Header simplification (fixed size of 40 bytes)
  Better support for options
  Improved Security capabilities
  Support for packet priority
  Support for pseudo connections (using the flow label)
  Support very long datagrams

## Slide 451: IPv6 Protocol Features
D
ata Communication Networks 115
Version: Always set to 6
Priority: Handle packets with different classes of service
  0-7 non-real-time (flow controlled)
  8-15 real-time (no flow control)
Flow: flow label which is used for flow-driven routing
Payload Length: packets with size >64k are supported
Next Header: Headers can optionally be extended over multiple packets.

## Slide 452: Multi Protocol Label Switching
Multiprotocol Label Switching (MPLS) is a mechanism in high- performance telecommunications networks which directs and carries data from one network node to the next.
MPLS makes it easy to create "virtual links" between distant nodes. It can encapsulate packets of various network protocols.
In an MPLS network, data packets are assigned labels. Packet- forwarding decisions are made solely on the contents of this label, without the need to examine the packet itself. This allows one to create end-to-end circuits across any type of transport medium, using any protocol
MPLS requires a small overhead, while providing connection-
oriented services for variable-length frames.
Advanced Communication Networkss
116

## Slide 453: MPLS Operation
Advanced Data Netwsorwksapping
117
1a. Existing routing protocols (e.g. OSPF, IS-IS)
establish reachability to destination networks
1b. Label Distribution Protocol (LDP) establishes label to destination network mappings.
2. Ingress Edge LSR receives packet, performs Layer 3 value- added services, and “labels”
packets
3. LSR switches packets using label
4. Edge LSR at egress removes label and delivers packet

## Slide 454: Label Switching Example
Data Communication Networks
118

## Slide 455: Multi Protocol Label Switching
Advanced Communication Networkss
Forwarding Equivalency Class (FEC)
  The FEC is used to describe an association of discrete packets with a destination address and a class of traffic. It allows the grouping of packets into classes.
  The matching of the FEC with a packet is achieved by using a label to identify each FEC. For different classes of service, different FECs and their associated labels are used.
Label Switching Router (LSR)
  Forwards MPLS packets using label switching
  Capable of forwarding native IP packets
  Executes one or more IP routing protocols
  Participates in MPLS control protocols
  A group of LSRs with the same MPLS level forms an MPLS domain.
Label Switched Path (LSP)
  The path through one or more LSRs followed by packets in a particular FEC is called a label-switched path

## Slide 456: MPLS Advantages
Advanced Communication Networkss
Simplified header processing:
  It is not necessary for MPLS routers to inspect the packet’s network layer headers.
Rather, they are only required to do a table lookup and label replacement.
A network with a state
  Packets that enter the network from different routers are distinguishable, so that forwarding decisions that depend on the ingress router can be easily made.
  This is not true of conventional forwarding, since packets are memoryless about their ingress routers.
More flexible per packet operation
  The label table of an MPLS switch may contain more information than just the next hop and the new label for a particular FEC.
  For example, an entry may include the precedence or class of service predetermined for the corresponding FEC.
  On the contrary, conventional forwarding can only consider information encoded in the packet header.
Create a Network Path for Traffic Engineering
  To improve the performance it is sometimes desirable, rather than letting the route be chosen by dynamic routing algorithms from hop to hop in the network, to force a packet to follow a route that is explicitly chosen before the packet enters the network. This capability is necessary to support traffic engineering.

## Slide 457: MPLS Label
Labels are assigned by downstream routers
Labels are local to each path and change at each hop
When there is a hierarchy in the MPLS network, labels can be stacked. Only top level labels are used to process the packet
Label value contains:
  Info for next hop
  Operations to do on the label stack:
    Swap label
    Pop an entry off the label stack
    Replace top label and then push another label
Advanced Communication Networkss

## Slide 458: Data Communication Networks Application Layer
Communication Networkss
•1
DR.Eslami
Department of Electrical Engineering
Islamic Azad University،Science And Research Branch

## Slide 459: Domain Name System
DNS is a hierarchical distributed database used to map host names
to IP addresses
To map a name an application calls a (local) library procedure called resolver
The resolver sends a UDP packet to a local DNS server
This server returns, possibly after consulting with other DNS
servers, the IP address to the application

## Slide 460: Domain Name System
DNS Name Space
  Naming scheme is hierarchical e.g. www.sharif.ac.ir
    ir is top level domain (TLD)
    sharif is sub domain and represents all the nodes under it
  Leaves of the tree represent domains which have no sub domain
  Naming follows organizational boundaries, not physical (network) ones

## Slide 461: DNS Name Space
Getting a name like sharif.ac.ir requires registration with the ac.ir
domain manager
After that sub domains can be added freely: ee.sharif.ac.ir
Names are case insensitive
DNS Database
  Every domain name has a set of corresponding resource records in the database
  For a single host: just record its IP address, but many other records exist
  When a resolver gives name to DNS, it gets back the associated resource records

## Slide 462: DNS Name Space
DNS resource record
  Domain-name: search key
  Time-to-live: indicates how stable the entry is in terms of seconds (needed for caching) e.g. 86400 seconds (= 1 day)
  Type: different types of resource records have been defined
  Class: always IN for internet information
  Value: Returned value
Example:
  relay1.bar.foo.com, static, A, IN, 145.37.93.126
  This means: IP Address of relay1.bar.foo.com is 145.37.93.126
Domain name | Time to live | Type | Class | Value

## Slide 463: DNS Server Types
Root DNS servers
Root name servers provide the IP addresses of the TLD servers.
Top-level domain (TLD) servers
Every top-level Domain has a top-level Domain Server
TLD servers provide the IP addresses for authoritative DNS servers.
Authoritative DNS servers
Every organization with publicly accessible hosts (such as Web servers and mail servers) on the Internet must provide publicly accessible DNS records that map the names of those hosts to IP addresses.
Data Communication Networks
6

## Slide 464: DNS Name Servers
The DNS name space is split into non overlapping zones.
A zone usually has 1 primary name server, and multiple secondary
ones, which get their information from the primary one.
Note: cs.yale.edu and yale.edu have separate name servers

## Slide 465: Name Resolution Example
The workstation annie asks its configured name server, dakota, for
www.nominum.com’s address
What’s the IP address of www.nominum.com?
annie.west.sprockets.com
ping www.nominum.com.
dakota.west.sprockets.com

## Slide 466: Name Resolution Example
The name server dakota asks a root name server, m, for www.nominum.com’s
address
annie.west.sprockets.com
ping www.nominum.com.
m.root-servers.net
dakota.west.sprockets.com
What’s the IP address of www.nominum.com?

## Slide 467: Name Resolution Example
The root server m refers dakota to the com name servers
This type of response is called a “referral”
annie.west.sprockets.com
ping www.nominum.com.
m.root-servers.net
dakota.west.sprockets.com
Here’s a list of the com name servers. Ask one of them.

## Slide 468: Name Resolution Example
f.gtld-servers.net
annie.west.sprockets.com
ping www.nominum.com.
m.root-servers.net
dakota.west.sprockets.com
The name server dakota asks a com name server, f, for
www.nominum.com’s address
What’s the IP address of www.nominum.com?

## Slide 469: Name Resolution Example
f.gtld-servers.net
annie.west.sprockets.com
ping www.nominum.com.
m.root-servers.net
dakota.west.sprockets.com
The com name server f refers dakota to the nominum.com name servers
Here’s a list of the nominum.com name servers.
Ask one of them.

## Slide 470: If the Name doesn’t exist
ping www.nominum.com.
annie.west.sprockets.com
f.gtld-servers.net
m.root-servers.net
dakota.west.sprockets.com
Here’s the address of www.nominum.com

## Slide 471: Name Resolution Example
ns1.sanjose.nominum.net
f.gtld-servers.net
annie.west.sprockets.com
ping www.nominum.com.
The name server dakota asks a nominum.com name server, ns1.sanjose, for
www.nominum.com’s address
What’s the IP address of www.nominum.com?
m.root-servers.net
dakota.west.sprockets.com

## Slide 472: Name Resolution Example
The nominum.com name server ns1.sanjose responds with
www.nominum.com’s address
f.gtld-servers.net
annie.west.sprockets.com
ping www.nominum.com.
m.root-servers.net
dakota.west.sprockets.com
ns1.sanjose.nominum.net
Here’s the IP address for www.nominum.com

## Slide 473: Name Resolution Example
The name server dakota responds to annie with www.nominum.com’s
address
Here’s the IP address for www.nominum.com
ns1.sanjose.nominum.net
f.gtld-servers.net
annie.west.sprockets.com
ping www.nominum.com.
m.root-servers.net
dakota.west.sprockets.com

## Slide 474: Name Lookup Sequence
DNS Records are cached in your computer as well as your ISP

## Slide 475: Electronic Mail
Important E-mail components:
  Simple Mail Transfer Protocol (SMTP).
  Main Server
  User agents

## Slide 476: Simple Mail Transfer Protocol (SMTP)
SMTP is the principal application-layer protocol for Internet
electronic mail.
It uses the reliable data transfer service of TCP to transfer mail from the sender’s mail server to the recipient’s mail server.

## Slide 477: Mail Access Protocols
Post Office Protocol (POP)
The Post Office Protocol provides access for a user client application to a mailbox maintained on a mail server.
The protocol supports download and delete operations for messages.
Internet Message Access Protocol (IMAP)
The Internet Message Access Protocol is an application layer Internet protocol that allows an e- mail client to access email on a remote mail server
Data Communication Networks
20

## Slide 478: World Wide Web
Web is framework for accessing linked documents
  Web servers provide documents (pages)
  Web browsers view the documents
  Pages are linked using hypertext techniques
Web idea comes from CERN, Geneva (1989)
WWW consortium was set up by CERN and MIT (1994) to organize and standardize

## Slide 479: World Wide Web: Architecture
Web pages are viewed by client-side programs called “browsers” (Chrome, Firefox)
Browsers key functions:
  Interact with the web servers using Hyper Text Transfer Protocol (HTTP) to fetch the desired content and data
  Display the content in a proper format to the user
  Interact with the user to receive user data (click on the page, typed text, etc)
  Interact with the helper applications on the user computer to handle the content properly
  Caching of the contents

## Slide 480: WWW Server Side
Hypertext transfer Protocol : HTTP
  HTTP is ASCII based protocol
Two types of requests:
  without or with protocol version
  e.g.: GET /hypertext/WWW/pages.html HTTP/1.0
Several built-in HTTP request methods

## Slide 481: WWW Server Side
WWW Pages
  Pages are written in HTML: HyperText Markup Language
  Markup commands are not hidden
  HTML editors are usually used to create and edit HTML pages
  Multiple versions of HTML have been developed with new features added on over time.

## Slide 482: Example of HTML page

## Slide 483: Example of HTML page

## Slide 484: Uniform Resource Locator: URL
WWW uses ULRs to locate pages
Example: http://sina.sharif.ac.ir/index.html
URL contains 3 parts:
  protocol name:
    HTTP, FTP, news, mailto, or file
  server name: sina.sharif.ac.ir
  page (file) name: Index.html

## Slide 485: Browsing the Web
Protocol steps:
  Browser determines URL
  Browser asks DNS to map server name to IP address
  Browser makes TCP connection to server IP address, port 80
  Browser sends GET ‘URL’ command
  Server sends page (file) index.html

## Slide 486: Server Side
Functions of the web server:
  Resolve the name of the Web page requested.
  Perform access control on the Web page.
  Check the cache.
  Fetch the requested page from disk or run a program to build it.
  Determine the rest of the response (e.g., the MIME type to send).
  Return the response to the client.
  Make an entry in the server log.
Key challenges:
  Speed
  Scalability
Solutions:
  Cache
  Load Balancing

## Slide 487: Server-Side Dynamic Web Pages
Many web interactions such as web search requires a program to generate
the content based on user data.
A program should run on the server side that interacts with user generated data.
Example: Search Engines such as google.com

## Slide 488: Server-Side Programming Languages
Programming languages oriented toward interfacing between the web and
the server database
Run on the server and generates dynamic web pages on the request of the client
Examples:
  PHP
  Python
  Java Script

## Slide 489: Client-Side Dynamic web Pages
Idea: Download a code that runs on the client side and interacts with user locally
Java Script
  A scripting language with some similarities to Java
Java applets:
  Applets are downloaded and then run locally
  Applets are written in JAVA bytecode and interpreted by a Java Virtual Machine (JVM)
  Interpreter has to guarantee security
  The objective has been to allow JAVA bytecodes to run on all machines that have a JVM